## Slide 2: Objectives
Goals of an OS
Different ways of designing an OS
x86 hardware

## Slide 3: Tentative lecture plan
x86 hardware and Unix model
Security in computer systems
Exokernel
Microkernel
Information flow control
HiStar OS
Managed languages
Singularity OS
Distributed systems
Barrelfish OS
Embedded OS

## Slide 4: What is an OS?
OS is a software that sits between hardware and applications and provides interfaces to applications for accessing hardware

## Slide 5: What is an application?
example.c
int main(int argc, char *argv[]) {
int fd = open(argv[1], O_CREAT);
write(fd, “hello world”, 11);
close(fd);
return 0;
}
gcc example.c
./a.out
a.out is an application.

## Slide 6: What is an application?
Firefox
Terminal
Power point
etc.

## Slide 7: Hardware
Disk
Network device
RAM
CPU
Monitor
Keyboard
etc.

## Slide 8: OS interface
example.c
int main(int argc, char *argv[]) {
int fd = open(argv[1], O_CREAT);
write(fd, “hello world”, 11);
close(fd);
return 0;
}

## Slide 9: Disk interface
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
write_to_sector(0)
write_to_sector(7)
read_from_sector(9)
Notes: The disk interface is the sequence of sectors. In this example, the sector size is 512 bytes. The disk interface allows programmers to read/write from/to sectors.

## Slide 10: OS interface
fd = open(argv[1], O_CREAT);
write(fd, “hello world”, 11);
Even though the entire file is not stored in consecutive sectors, the OS interfaces allow you to access the file sequentially
Notes: OS interface is the file system. A file is divided into the contiguous blocks, where the block size is equal to sector size. Blocks can be stored in random sectors. The OS hides the complexity of blocks to sector translation from the programmers.

## Slide 11: OS interface
fd = open(argv[1], O_CREAT);
write(fd, “hello world”, 11);
Even though the entire file is not stored in consecutive sectors, the OS interfaces allow you to access the file sequentially
BLOCK | SECTOR
0 | 15
1 | 23
2 | 43
3 | 29
… | …
Notes: The OS keeps the mapping from blocks to sectors.

## Slide 12: What does an OS do?
OS is a library
  write_to_console, write, read, etc.

## Slide 13: write_to_console
An API that writes a character to the display device
Applications are not allowed to use their own implementation of write_to_console
  Different from the standard library where you can use a custom implementation of library functions, e.g., strcpy, strcmp, etc.

## Slide 14: What does an OS do?
OS is a library
  write_to_console
Enforce use of OS library
  Access to hardware recourses is only permitted through the OS library APIs
Notes: We can not let the applications access the console directly, because in that case, an application can hijack the console and prevent other applications from using them.

## Slide 15: Isolation
An application can’t see the data of other applications
Applications are untrusted
  A gaming application can’t see your password in a banking application
OS is trusted
  If our OS is malicious, then it can allow malicious applications to steal our passwords
  We all trust our OS to protect us from malicious software

## Slide 16: What does an OS do?
OS is a library
  write_to_console
Enforce use of OS library
  Access to hardware recourses is only permitted through the OS library APIs
Isolation

## Slide 17: Sharing of hardware resources
E.g., OS decides which application is going to use the display device at a given time

## Slide 18: What does an OS do?
OS is a library
  write_to_console
Enforce use of OS library
  Access to hardware recourses is only permitted through the OS library APIs
Isolation
Share hardware resources among applications

## Slide 19: What is inside a.out?
gcc -m32 -fno-pic example.c
objdump -dx a.out |less
a.out contains CPU (x86) instructions
Instructions are stored in memory

## Slide 20: Physical address space
Each byte in the main memory (RAM) has an address
Using 32 bits, we can generate 232 unique values
In x86 32-bit architecture, the physical address space contains 232 addresses

## Slide 21: Physical address space
32-bit memory
mapped devices
unused
Extended memory
BIOS ROM
16-bit devices
VGA display
Low memory
0xFFFFFFFF (4 GB)
0x00000
depends on RAM
0x10000 (1 MB)
0x0F000 (960 KB)
0x0C000 (768 KB)
0x0A000 (768 KB)

## Slide 22: Registers
A general-purpose register can hold a 32-bit value (data/address)
X86 has eight general-purpose registers
  EAX, ECX, EDX, EBX, ESI, EDI, EBP, ESP

## Slide 23: Registers
 | AH | AL
 | BH | BL
 | CH | CL
 | DH | DL
 | SI
 | DI
 | BP
 | SP
0
7
15
31
AX | EAX
BX | EBX
CX | ECX
DX | EDX
 | ESI
 | EDI
 | EBP
 | ESP
16 bit
32 bit

## Slide 24: What is inside a.out?
gcc -m32 -fno-pic example.c
objdump -dx a.out |less
a.out contains CPU (x86) instructions
Instructions are stored in memory
CPU reads the instructions from memory and executes them

## Slide 25: x86 CPU interface
The instruction pointer (EIP register) contains the memory address where the next instruction is stored
while (1) {
instruction = fetch(EIP);
execute instruction;
if (instruction doesn’t modify EIP) {
EIP = EIP + length(instruction);
}
}

## Slide 26: x86 instructions
Branch instructions can modify EIP
  call, ret, jmp, je, jne, etc. are branch instructions
  Transfer the control to other parts of the code
Instructions can read/write from/to physical address space
Instructions can perform arithmetic or logical operations on registers and physical addresses

## Slide 27: x86 instructions
add $1, %eax
An instruction consists of an opcode followed by one or more operands
Operands are constants, registers, direct memory addresses, and indirect memory addresses

## Slide 28: x86 instructions
add $1, %eax
The instructions are the sequence of bytes
The above notation is used by the programmers to write an assembly program that can be converted into the bytecode using an assembler

## Slide 29: Register mode
movl %eax, %edx
%edx = %eax
b,w,l denotes the size of operands
AT&T (gcc) syntax: opcode src, dst

## Slide 30: Register mode
movb %al, %bl
%bl = %al
b,w,l denotes the size of operands
AT&T (gcc) syntax: opcode src, dst

## Slide 31: Register mode
movw %ax, %bx
%bx = %ax
b,w,l denotes the size of operands
AT&T (gcc) syntax: opcode src, dst

## Slide 32: Immediate
movl $0x123, %eax
%eax = 0x123;

## Slide 33: Direct memory access
movl 0x123, %edx
%edx = *((int32*)0x123);
(memory read)

## Slide 34: Direct memory access
movl %edx, 0x123
*((int32*)0x123) = %edx;
(write to memory)

## Slide 35: Indirect memory operand
disp(base, index, scale)
disp: 32 bit signed integer
base, index : register
scale: 1,2,4,8
address: disp + base + (index * scale)

## Slide 36: Indirect memory access
movl (%ebx), %edx
%edx = *((int32*)%ebx)
(memory read)

## Slide 37: Indirect memory access
movl 4(%ebx), %edx
%edx = *((int32*)(%ebx+4))

## Slide 38: Indirect memory access
movl (%ebx,%ecx,4), %edx
%edx = ((int32*)(%ebx))[%ecx]

## Slide 39: Indirect memory access
movl (%ebx,%ecx,1), %edx
%edx = *((int32*)(%ebx + %ecx))

## Slide 40: Indirect memory access
movl %edx, (%ebx,%ecx,1)
*(int32*)(%ebx + %ecx) = %edx
(write to memory)

## Slide 41: Indirect memory access
movl $0x0, (%ebx,%ecx,1)
*(int32*)(%ebx + %ecx) = 0x0
do we need to specify the “l” suffix

## Slide 42: Indirect memory access
mov $0x0, (%ebx,%ecx,1)
is ambiguous
Notes: It is not evident from this instruction that, whether we want to store 1,2, or 4-byte value (0) into the destination memory address. A “b”, “w”, or “l” suffix is required to eliminate this ambiguity.

## Slide 43: Indirect memory access
mov %eax, (%ebx,%ecx,1)
is not ambiguous
Notes: Here, we know that %eax contains a 4-byte value.

## Slide 44: Data movement instructions
READ | WRITE | ADDRESS
mov 0x123, %eax | mov %eax, 0x123 | 0x123
mov (%ebx), %eax | mov %eax, (%ebx) | %ebx
mov (%ebx, %edx, 4), %eax | mov %eax, (%ebx, %edx, 4) | %ebx + %edx * 4
mov (,%edx, 4), %eax | mov %eax, (, %edx, 4) | %edx * 4
mov 0x100(%ebx, %edx, 4), %eax | mov %eax, 0x100(%ebx, %edx, 4) | 0x100 + %ebx + (%edx * 4)

## Slide 45: jmp instruction
jmp rel32 // unconditional jump
EIP = EIP + rel32
rel32 is 32 bit signed integer
C equivalent:
goto label;
Notes: jmp instruction is an unconditional jump. This instruction sets the EIP to EIP + rel32.

## Slide 46: x86 EFLAGS register
Section-3.4.3 in Intel’s manual-1 (classroom)

## Slide 48: EFLAGS
Some instructions set certain bits in the EFLAGS register
  Whether the last arithmetic instruction overflowed (OF)
  Was positive/negative (SF)
  Was zero / not zero (ZF)
  Carry/borrow on add/subtract (CF)

## Slide 49: Compare
cmp %eax, %edx
Perform %edx - %eax
Sets the flags in the EFLAGS register accordingly
If %edx and %eax are equal the ZF will be set
If %edx > %eax then CF will not be set
if %edx < %eax the CF (borrow) will be set

## Slide 50: jcc – jump if condition is met
je rel32 // jump on equal
if (last operation was equal) //(ZF = 1)
EIP = EIP + rel32
Notes: If the ZF is set, then src2 = src1. The x86 processor looks at the eflags register to find the value of zero flag(ZF). If ZF is set, then the x86 processor sets the EIP to the target address (EIP + rel32).

## Slide 51: jcc – jump if condition is met
ja rel32 // jump on above
if (in last operation src2 > src1) // CF = 0 and ZF = 0
EIP = EIP + rel32
Notes: If the ZF is set then src2 = src1. ja jumps to the target address (EIP + rel32) only if src2 > src1. The x86 processor looks at the eflags register to find the value of the carry flag(CF) and the zero flag(ZF). If both of them are not set, then it sets the EIP to the target address (EIP + rel32).

## Slide 52: jcc – jump if condition is met
jb rel32 // jump on below
if (in last operation src2 < src1) // CF = 1
EIP = EIP + rel32

## Slide 53: jcc – jump if condition is met
jae rel32 // jump on above or equal
if (in last operation src2 >= src1) // CF = 0 or ZF = 1
EIP = EIP + rel32

## Slide 54: Example
if (%eax < %edx) {
}

## Slide 55: Example
if (%eax < %edx) {
}
cmp %eax, %edx
jbe label // jump if %edx <= %eax
// if body
label:

## Slide 56: Example
if (%eax < %edx) { //if body }
else { //else body }
Notes: After if body, we need to insert an unconditional jump to skip the else body.

## Slide 57: Example
if (%eax < %edx) { //if body }
else { //else body }
cmp %eax, %edx
jbe label1 // jump if %edx <= %eax
// if body
jmp label2:
label1:
// else body
label2:
Notes: After if body, we need to insert an unconditional jump to skip the else body.

## Slide 58: Addition
add %eax, %edx
%edx = %edx + %eax

## Slide 59: Addition
add %eax, (%edx)
*((int32*)%edx) = *((int32*)%edx) + %eax;

## Slide 60: Logical AND
and %eax, %edx
%edx = %edx & %eax;

## Slide 61: Logical AND
and %eax, (%edx)
*((int32*)%edx) = %edx & *((int32*)%eax);

## Slide 62: References (available on classroom)
A Guide to Programming Intel IA32 PC Architecture
Intel manual - 2

## Slide 63: Next homework
Read Intel manual-2 to find the meaning of some x86 instructions
The Intel syntax is different from AT&T syntax
  In Intel’s syntax, the first operand is the destination