## Slide 2: Today’s topics
Midterm format
Reliable data transfer protocol
Go-Back-N (GBN)

## Slide 3: References
Read chapter-3.4 from the Kurose and Ross book

## Slide 4: Finite state machine (FSM)
FSM has one or more states, and there is one starting state
Each state is waiting for some event to happen
Arrow represents a transition from the current state to a state in the FSM
A transition is triggered by an event and the corresponding action
The arrows are labelled with an event and the corresponding action
The events and actions are separated by a horizontal line
The initial state is represented by a dashed line

## Slide 5: Finite state machine (FSM)
The starting state at the sender end waits for the rdt_send event, which is triggered when the application sends data to the receiver
The starting state at the client end waits for the rdt_rcv event, which is triggered when the network layer hands the data to the transport layer

## Slide 6: Other APIs
pkt = make_pkt(data, …)
  make a packet from data
udt_send(packet)
  send packet on the communication channel
  udt stands for unreliable data transfer
data = extract(packet)
  extract data from the packet
deliver(data)
  deliver data to the application

## Slide 7: rdt3.0
Let’s allow packet loss, in addition to the packet corruption
What modifications are needed in rdt2.1?

## Slide 8: rdt3.0 (packet loss)

## Slide 9: rdt3.0 (ACK loss)

## Slide 10: rdt3.0 (ACK delayed)

## Slide 11: rdt3.0 (stop-and-wait)
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 12: rdt3.0 (stop-and-wait)
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
ack1
send ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
pkt1
(ignore)
rcv ack1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 13: rdt3.0
Let’s allow packet loss
What modifications are needed in rdt2.1?
  Introduce a timeout at the sender
    If an ACK isn’t received during a given period of time, resend the packet
  What value should we pick for the timeout?
    What is the problem when the timeout is very small?
    What is the problem when the timeout is very large?
    What should be an ideal timeout?

## Slide 14: rdt3.0
Let’s allow packet loss.
What modifications are needed in rdt2.1?
  Introduce a timeout at the sender
    If an ACK isn’t received during a given period of time, resend the packet
  What value should we pick for the timeout?
    What is the problem when the timeout is very small?
      Unnecessary retransmissions
    What is the problem when the timeout is very large?
      Retransmissions are delayed. Poor performance.
    What should be an ideal timeout?
      It should be slightly more than RTT. However, RTT is not fixed and may vary due to the change in load at intermediate gateways, so finding an ideal timeout might be tricky.

## Slide 15: rdt3.0 sender

## Slide 16: rdt3.0 receiver

## Slide 17: rdt3.0 sender
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
L
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 18: rdt3.0 receiver
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
data = extract(rcvpkt)
deliver(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
data = extract(rcvpkt)
deliver(data)
sndpkt = make_pkt(ACK0, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(ACK0, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK0, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 19: rdt3.0
rdt3.0 is also called a stop-and-wait protocol
  The sender sends a packet if and only if it is convinced that the receiver has received the previous packet

## Slide 20: rdt3.0 (stop-and-wait)
no loss

## Slide 21: rdt3.0 (stop-and-wait)
packet loss

## Slide 22: rdt3.0 (stop-and-wait)
ACK loss

## Slide 23: rdt3.0 (stop-and-wait)
ACK delayed

## Slide 24: rdt3.0 (stop-and-wait)
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 25: rdt3.0 (stop-and-wait)
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
ack1
send ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
pkt1
(ignore)
rcv ack1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 26: rdt3.0
Assumption:
  The rdt3.0 assumes that if a packet is not lost, it will be received in the same order in which it was sent, i.e., the network will not reorder the packet

## Slide 27: rdt3.0 (stop-and-wait)

## Slide 28: rdt3.0 (stop-and-wait)
rcv pkt1_0
send ack0
pkt1_0
sender
receiver
rcv pkt2_1
rcv pkt1_0
send ack1
send ack0
send pkt0
rcv ack1
send pkt0
pkt1_0
pkt3_0
ack1
ack0
pkt2_1
timeout
resend pkt0
rcv ack0
send pkt1
ack0
rcv pkt3_0
(detect duplicate)
send ack0
ack0
rcv ack0
rcv ack0
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 29: rdt3.0 reordering
Assumption:
  The rdt3.0 assumes that if packet is not lost, it will be received in the same order in which it was sent, i.e., the network will not reorder the packet
    Let’s consider the following example
      A user wants to send three packets: pkt1_0, pkt2_1, and pkt3_0 with sequence numbers 0, 1, and 0, respectively. pkt1_0 somehow took a very long path; consequently, it was retransmitted and received at the receiver end. After that, the sender sends pkt2_1, which was also successfully delivered to the receiver. Then the sender sends pkt3_0, but this time, before pkt3_0 can reach the receiver, pkt1_0 arrives at the receiver. Because the receiver was hoping to accept a packet with sequence number zero, it accepts pkt1_0, but discards pkt3_0 if it arrives just after pkt1_0 (because it was expecting a packet with sequence number 1 after receiving pkt1_0).

## Slide 30: rdt3.0 reordering
How to fix the reordering problem?

## Slide 31: rdt3.0 reordering
How to fix the reordering problem?
  Use a unique sequence number for each packet

## Slide 32: rdt3.0 reordering
How to fix the reordering problem?
  Use a unique sequence number for each packet
    But the sequence number is of finite width

## Slide 33: rdt3.0 reordering
How to fix the reordering problem?
  Use a unique sequence number for each packet
    But the sequence number is of finite width
      Ensure that a packet is thrown out of the network after a maximum interval
        This is actually the case. The IP layer adds a time-to-live field that discards the packet if it traverses through a certain number of hops
        Usually, the maximum lifetime of the packet is 180 seconds
        We need to ensure that the sequence number doesn’t exhaust in 180 seconds in order to fix the reordering problem.
As of now, we will assume that the reordering problem doesn’t exist in our subsequent discussions

## Slide 34: RDT 3.0 utilization
Utilization: the fraction of time sender is actually busy sending the packets into the channel

## Slide 35: rdt3.0: stop-and-wait utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Utilization at sender:
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 36: rdt3.0: stop-and-wait utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Utilization at sender:
Transmission time = 1Kb/1Mb = 1 ms
Ack received after = 10 ms
Out of 10 ms, the sender is busy sending the packets is 1 ms.
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 37: rdt3.0: stop-and-wait utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Utilization at sender:
where,
L is the packet size
R is the transmission rate
RTT is round-trip time (RTT includes all types of delays for a very small packet)
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 38: How can we improve the performance?

## Slide 39: How can we improve the performance?
Pipelining
  Send multiple packets instead of one without waiting for an acknowledgement

## Slide 40: Pipelining
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Sending three packets instead of one
Utilization at sender:
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 41: Pipelining
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Sending three packets instead of one
Utilization at sender:
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 42: Pipelining
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Sending ten packets instead of one
Utilization at sender:
…
last bit of 10th packet arrives, send ACK
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 43: Pipelining
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
RTT = 9 ms
Transmission rate: 1 Mbps
Packet size: 1 Kb
Sending ten packets instead of one
Utilization at sender:
last bit of 10th packet arrives, send ACK
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 44: Utilization
The optimal number of packets (for best utilization) in the pipeline mode depends on the RTT and the transmission rate

## Slide 45: Pipelining
How long does the sender need to keep a copy of a sent packet in stop-and-wait and pipeline mode?

## Slide 46: Pipelining
How long does the sender need to keep a copy of a sent packet in stop-and-wait and pipeline mode?
  Until the acknowledgement arrives
Is the memory overhead at the sender higher in the pipeline mode compared to the stop-and-wait mode?

## Slide 47: Pipelining
How long does the sender need to keep a copy of a sent packet in stop-and-wait and pipeline mode?
  Until the acknowledgement arrives
Is the memory overhead at the sender higher in the pipeline mode compared to the stop-and-wait mode?
  Yes, because the kernel needs to keep a copy of all unacknowledged packets in transit, which is just one in the stop-and-wait mode
Therefore, for good performance, the total number of unacknowledged packets in the pipeline mode must fit in the sender’s queue

## Slide 48: Pipelining
How can we implement pipelining?
  How many packets should be allowed in the pipeline?
  What information needs to be saved at the sender’s end?
  What information needs to be saved at the receiver end?
  What additional information needs to be added to the packets?
  What is the format of acknowledgements?
  How frequently does the receiver need to send the acknowledgements?

## Slide 49: Pipelining (sender and receiver)

## Slide 50: Go-Back-N
The Go-Back-N scheme allows at most N unacknowledged packets in the pipeline.

## Slide 51: Go-Back-N

## Slide 52: Go-Back-N
is the sequence number of the first unacknowledged packet in the queue.
All packets before can be removed from the queue.
All the packets outside the window size N, starting from , are not allowed to be sent by the Go-Back-N protocol.
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 53: Go-Back-N (GBN)
The maximum number of unacknowledged packets in GBN is called the window size
The GBN protocol is also an example of a sliding-window protocol

## Slide 54: Go-Back-N
rcv_base
received and ACKed
Out-of-order: received but not ACKed
Not received
Receiver view of sequence number space:
…
…
The receiver waits for a packet with sequence number .
All the previous packets before have been received and acknowledged.
Some packets with a sequence number higher than the could have been received and queued by the receiver. However, the Go-Back-N protocol doesn’t require the receiver to queue out-of-order packets.
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 55: GBN Sender
Initialization
  is set to the first available sequence number, i.e., 1
  is set to the first unacknowledged sequence number, i.e., 1
  The sender window is empty when
  Maximum window size is

## Slide 56: GBN Sender
During send:
  The packet is discarded if there are already N unacknowledged packets
  Add to packet
  if { start timer }
On timeout:
  resend all packets from to
  start the timer
On receiving acknowledgement
  fetch from ACK
  If

## Slide 57: GBN Receiver
Initialization
  is initialized to 1, i.e., initially the receiver is expecting a packet with sequence number 1
On receive
  fetch from the packet
    If
    else {drop the packet; }

## Slide 58: GBN in action
window size=4
The third packet is lost

## Slide 59: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
pkt 2 timeout
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 60: Finite state machine
For variable initialization, we add an action that is not preceded by any event
The initialization action is taken when the execution reaches a particular state for the first time

## Slide 62: GBN sender (FSM)
Wait for call from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
if (nextseqnum<send_base+N) {
sndpkt[nextseqnum] = make_pkt(data, csum, nextseqnum)
udt_send(sndpkt[nextseqnum])
if (send_base == nextseqnum)
start_timer
nextseqnum++
} else
refuse_data(data)
rdt_send(data)
sender
ackseqno = getackseqnum(rcvpkt)
if (ackseqno >= send_base) {
send_base = ackseqno + 1
stop_timer
if (nextseqno != send_base)
start_timer
}
Copyright © 2010-2025 J.F. Kurose, K.W. Ross
send_base = 1
nextseqnum = 1
timeout
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
rdt_rcv(rcvpkt) && corrupt(rcvpkt)

## Slide 63: GBN receiver (FSM)
Wait for call from below
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) || ! hasseqnum(rcvpkt, rcv_base))
data = extract(rcvpkt)
deliver(data)
sendpkt = make_pkt(rcv_base, ACK, chksum)
udt_send(sendpkt)
rcv_base++
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt) && hasseqnum(rcvpkt, rcv_base)
receiver
udt_send(sendpkt)
Copyright © 2010-2025 J.F. Kurose, K.W. Ross
rcv_base = 1