## Slide 2: Today’s topics
TCP SACK homework
Flow control
TCP connection management
Congestion control

## Slide 3: References
Read Chapter-3.5.6, 3.6 from the Kurose and Ross book

## Slide 4: TCP SACK homework
What are TCP SACK acknowledgments?

## Slide 5: TCP SACK homework
What are TCP SACK acknowledgments?
  A receiver uses TCP SACK acknowledgements to inform the sender regarding the range of sequence numbers received by it beyond the cumulative acknowledgment number
Where are TCP SACK acknowledgments stored?

## Slide 6: TCP SACK homework
What are TCP SACK acknowledgments?
  A receiver uses TCP SACK acknowledgements to inform the sender regarding the range of sequence numbers received by it beyond the cumulative acknowledgment number
Where are TCP SACK acknowledgments stored?
  In the optional TCP header

## Slide 7: TCP SACK homework
A TCP optional header looks as follows
kind | len | value | kind | len | value | kind | len | value | ….
kind and len are of one byte. The value could be of variable length.
kind 0 and 1 are not followed by len and value.
kind 0 →end of option (you can stop parsing)
kind 1 → no operation (nop, skip the byte)
kind 0 and 1 are followed by another kind (if the current byte is not the end of the header)

## Slide 8: TCP SACK homework
kind 5 is used for TCP SACK acknowledgments
Each SACK range is eight bytes long. You can find the number of ranges using the value of len stored in the subsequent byte.
  len = length of value + 2
In this assignment, you are to implement
  void print_tcp_options(unsigned char *options, size_t len)
    options points to the TCP optional header
    len is the length of the optional header
    Objective: print TCP SACK ranges stored in the header

## Slide 9: TCP SACK homework
Drop packets using sudo tc qdisc add dev eth0 root netem loss 10% to trigger SACK acknowledgements
Measure the performance of transferring a large file with and without SACK in a congested network

## Slide 10: Flow control
If the application can not consume data at the rate it is arriving at the receiver, then the packets can be dropped if the receive window is full
Let’s consider the example on the next slide

## Slide 11: Flow control
N = 1000 Kb
rcv_base = 500 Kb
send_base = 400 Kb
nextseqnum = 600 Kb
How much more data can the sender send?
What if the application has not yet received any data? How much more data can the receiver actually receive?
What will happen to the data post 1000 Kb at the receiver?
How can we prevent packet drop?
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 12: Flow control
N = 1000 Kb
rcv_base = 500 Kb
send_base = 400 Kb
nextseqnum = 600 Kb
How much more data can the sender send?
800 Kb
What if the application has not yet received any data? How much more data can the receiver actually receive?
500 Kb after recv_base
What will happen to the data post 1000 Kb at the receiver?
dropped
How can we prevent packet drop?
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 13: Flow control
To prevent the sender from overflowing its buffer, the receiver advertises the free space remaining in its buffer to the sender
Let’s say:
  is the size of the receive buffer
  : the sequence number of the last byte read by the application
  : the sequence number of the last byte stored in the receiver buffer
  What should be the advertised window size?

## Slide 14: Flow control
To prevent the sender from overflowing its buffer, the receiver advertises the free space remaining in its buffer to the sender
Let’s say:
  is the size of the receive buffer
  : the sequence number of the last byte read by the application
  : the sequence number of the last byte stored in the receiver buffer
  What should be the advertised window size?
      Assuming that the sequence numbers are not reused

## Slide 15: Flow control
is dynamic
The sender doesn’t send data post
How does the receiver inform the sender about ?
The TCP header contains the receive window field
  This field is set to in the acknowledgements

## Slide 16: Flow control
What will happen if the receiver advertises as zero?

## Slide 17: Flow control
What will happen if the receiver advertises as zero?
  The sender will not send any data
  Consequently, acknowledgements are sent only for old data
    If the application hasn’t read anything, the will still be zero
  So, even if the receive queue has free space after some time when everything has been acknowledged, the sender has no way to know about this?
  How can we fix this?
    TCP allows the sender to send one byte, even if is zero.
    The updated will be received in the acknowledgements

## Slide 18: keeping the pipe full
Suppose A and B are connected using a 100 Kbps link and the RTT is 100 ms. What should be the window size in order to keep the sender busy all the time, if it has enough data to send?

## Slide 19: keeping the pipe full
Suppose A and B are connected using a 100 Kbps link and the RTT is 100 ms. What should be the window size in order to keep the sender busy all the time, if it has enough data to send?
For good performance, the window size should be at least equal to
  In practice, it could be more than to account for the RTT variation, delayed ACKs, or the application’s asynchronous behaviour in receiving the data

## Slide 20: TCP connection management
Establishing a connection
  Client sends a special packet with the SYN bit set to the server. The packet also contains an initial sequence number, say
  Server replies with SYN+ACK packet. The ACK contains , i.e., the first sequence number it expects. The packet also contains the initial sequence number of the segments from the server, say
  The client replies with ACK. The ACK contains , i.e., the sequence of the first byte it receives from the server. This segment may optionally contain data from the client as well.

## Slide 21: Three way handshake

## Slide 22: Two-way handshake
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 23: Two-way handshake
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 24: Two-way handshake
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 25: TCP three-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYN SENT
ESTAB
SYN RCVD
Client state
Server state
LISTEN
s = socket(PF_INET, SOCK_STREAM, 0)
s = socket(PF_INET, SOCK_STREAM, 0)
bind(s, &saddr, sizeof(saddr))
listen(s, MAX_PENDING)
new_s = accept(s, &caddr, &addr_len)
connect(s, &saddr, sizeof(saddr))
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 26: TCP connection management
Closing a connection
  The client or server can close the connection at their end in two steps
    Suppose A wants to close the connection with B
      A sends a packet with the FIN bit set to B
      B sends an ACK
      After this point, A can’t send packets to B, called half close
      However, A can receive packets and send acknowledgments
    After some time, B wants to close the connection with A
      B sends a packet with the FIN bit set to A
      A sends an ACK
      At this point, the connection has been closed completely
    Additionally, ACK can be combined with FIN
      e.g., if B also wants to close the connection after receiving a FIN from A, it can send FIN along with ACK.

## Slide 27: Closing a connection

## Slide 28: SYN flood attack
In a SYN flood attack, an attacker sends too many SYN segments to the server
On receiving a SYN segment, the TCP server may allocate resources, e.g., socket, send, and receive buffers, a separate thread, an initial sequence number, etc., and replies with a SYN+ACK to the client
However, the SYN+ACK segments never reach the attacker, and too many half-open connections exhaust the server resources, which is the main objective of the SYN flood attack
After the attack, the server won’t be able to service other legitimate clients

## Slide 29: SYN flood attack
SYN cookie approach aims to mitigate this attack
In this approach, the server doesn’t need to remember any state, not even the starting sequence number sent in the SYN+ACK segment
Can you think of a scheme using which the server can verify the initial sequence number in the legitimate ACK without remembering its earlier response?

## Slide 30: SYN cookie approach

## Slide 31: SYN cookie approach
In the SYN cookie approach, the TCP server doesn’t allocate any resources after receiving a SYN segment
The starting sequence number is computed using a hash function on source IP, destination IP, source port, destination port, and the server’s secret key
  initial_seqno = hash_fn(srcIP, dstIP, srcPort, dstPort, secretKey)
After receiving an ACK segment from the client, the server recomputes the initial sequence number using the same hash function
  In a legitimate ACK, the acknowledgment number must match the recomputed value + 1
    verify, ACK.ackno == hash_fn(srcIP, dstIP, srcPort, dstPort, secretKey) + 1
  At this point, the server allocates actual resources

## Slide 32: SYN cookie approach
Why is secretKey needed? What is the problem with the following hash function?
  hash_fn(srcIP, dstIP, srcPort, dstPort)

## Slide 33: SYN cookie approach
Why is secretKey needed? What is the problem with the following hash function?
  hash_fn(srcIP, dstIP, srcPort, dstPort)
If the secretKey is not part of the hash function, the attacker can recompute the sender’s sequence number, y, using the same hash_fn and send an ACK segment with y+1
  secretKey is preventing the attacker from computing y

## Slide 34: Congestion control
The flow control is done between the two communicating hosts
If a receiver can receive data at a rate R, then the sender is allowed to send at rate R
However, if multiple senders are sending at the full speed as allowed by the flow control, it is possible that the traffic intensity at an intermediate gateway is close to one or even more than one, causing packet drops. This condition is known as network congestion.

## Slide 35: Congestion control
A
B
G
C
D
5 Mbps
5 Mbps
2 Mbps
2 Mbps
1.5 Mbps
1.5 Mbps
A and B are connected to gateway G, which is connected to gateway C and D.
A is sending data to D, and B is sending data to C.
A and B are connected to G using a 5 Mbps link.
G is connected to C and D using a 2 Mbps link.
A and B are sending data at the rate of 1.5 Mbps.
What is the traffic intensity at G?
traffic intensity =

## Slide 36: Congestion control
A
B
G
C
D
5 Mbps
5 Mbps
2 Mbps
2 Mbps
1.5 Mbps
1.5 Mbps
A and B are connected to gateway G, which is connected to gateway C and D.
A is sending data to D, and B is sending data to C.
A and B are connected to G using a 5 Mbps link.
G is connected to C and D using a 2 Mbps link.
A and B are sending data at the rate of 1.5 Mbps.
What is the traffic intensity at G?
traffic intensity =
= = 0.75 (Good)
At what rate will C and D receive data =

## Slide 37: Congestion control
A
B
G
C
D
5 Mbps
5 Mbps
2 Mbps
2 Mbps
1.5 Mbps
1.5 Mbps
A and B are connected to gateway G, which is connected to gateway C and D.
A is sending data to D, and B is sending data to C.
A and B are connected to G using a 5 Mbps link.
G is connected to C and D using a 2 Mbps link.
A and B are sending data at the rate of 1.5 Mbps.
What is the traffic intensity at G?
traffic intensity =
= = 0.75 (Good)
At what rate will C and D receive data = 1.5 Mbps

## Slide 38: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
5 Mbps
5 Mbps

## Slide 39: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (assuming infinite queue size at G)
5 Mbps
5 Mbps

## Slide 40: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (assuming infinite queue size at G) = 2 Mbps
5 Mbps
5 Mbps

## Slide 41: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (assuming infinite queue size at G) = 2 Mbps
Will there be any difference from the previous case when A and B were sending at 1.5 Mbps, apart from the new receive rate?
5 Mbps
5 Mbps

## Slide 42: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (assuming infinite queue size at G) = 2 Mbps
Will there be any difference from the previous case when A and B were sending at 1.5 Mbps, apart from the new receive rate?
The packet will experience significant delays.
5 Mbps
5 Mbps

## Slide 43: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
traffic intensity = LA/R
average queueing delay
1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross
5 Mbps
5 Mbps

## Slide 44: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (if the queue size is finite) =
5 Mbps
5 Mbps
10% packets were dropped.

## Slide 45: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (if the queue size is finite) =
Depends on the packet drop rate. Let’s say 10% packets were dropped, the receive rate would be 1.8 Mbps.
5 Mbps
5 Mbps
10% packets were dropped.

## Slide 46: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (if the queue size is finite) =
Depends on the packet drop rate. Let’s say 10% packets were dropped, the receive rate would be 1.8 Mbps.
Can A and B send data at a higher rate to compensate for the packet loss?
5 Mbps
5 Mbps
10% packets were dropped.

## Slide 47: Congestion control
A
B
G
C
D
2 Mbps
2 Mbps
2 Mbps
2 Mbps
After some time, A and B are sending data at the maximum rate of 2 Mbps (window size / RTT) allowed by flow control (assuming no loss).
What is the traffic intensity at G?
= 1 (Bad)
At what rate will C and D receive data (if the queue size is finite) =
Depends on the packet drop rate. Let’s say 10% packets were dropped, the receive rate would be 1.8 Mbps.
Can A and B send data at a higher rate to compensate for the packet loss?
Yes, if a segment is lost within the advertised window, the sender can retransmit it as many times as necessary.
5 Mbps
5 Mbps
10% packets were dropped.