## Slide 2: Today’s topics
DHCP
NAT
IPv6

## Slide 3: References
Read Chapter-4.2, 4.3 from the Kurose and Ross book

## Slide 4: Subnet address
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 5: Who manages IP address?
Internet Corporation of Assigned Names and Numbers (ICANN)
Regional Internet Registries (RIRs)
Internet Service Providers (ISPs)
Organizations / Home Internet Users (e.g., IIITD / Individual)

## Slide 6: Assigning IP address
Let’s say, the ISP receives a subnet address 200.23.16.0/20 from RIR
When IIITD contacts its ISP for a range of IP addresses, the ISP can assign a subnet out of its allocated addresses to IIITD
  Say 200.23.16.0/23
Let’s say GB Pant asked the ISP to give it a range of addresses
  Can ISP give 200.23.17.0/23 to GB Pant?

## Slide 7: Assigning IP address
Let’s say, the ISP receives a subnet address 200.23.16.0/20 from RIR
When IIITD contacts its ISP for a range of IP addresses, the ISP can assign a subnet out of its allocated addresses to IIITD
  Say 200.23.16.0/23
Let’s say GB Pant asked the ISP to give it a range of addresses
  Can ISP give 200.23.17.0/23 to GB Pant?
    No, because IIITD addresses are also included in 200.23.17.0/23
  How about 200.23.18.0/23?

## Slide 8: Assigning IP address
Let’s say, the ISP receives a subnet address 200.23.16.0/20 from RIR
When IIITD contacts its ISP for a range of IP addresses, the ISP can assign a subnet out of its allocated addresses to IIITD
  Say 200.23.16.0/23
Let’s say GB Pant asked the ISP to give it a range of addresses
  Can ISP give 200.23.17.0/23 to GB Pant?
    No, because IIITD addresses are also included in 200.23.17.0/23
  How about 200.23.18.0/23?
    Yes, no overlap with IIITD

## Slide 9: Obtaining host address
Let’s say IIITD got 200.23.16.0/23
  Can we use 200.23.16.1 for user A and 200.23.16.2 for user B

## Slide 10: Obtaining host address
Let’s say IIITD got 200.23.16.0/23
  Can we use 200.23.16.1 for user A and 200.23.16.2 for user B
    Yes
  If the users know about the subnet, should we allow them to pick a random address for the pool of addresses allocated to IIITD

## Slide 11: Obtaining host address
Let’s say IIITD got 200.23.16.0/23
  Can we use 200.23.16.1 for user A and 200.23.16.2 for user B
    Yes
  If the users know about the subnet, should we allow them to pick a random address for the pool of addresses allocated to IIITD
    No, two users may end up assigning the same IP address
  IP assignment?

## Slide 12: Obtaining host address
Let’s say IIITD got 200.23.16.0/23
  Can we use 200.23.16.1 for user A and 200.23.16.2 for user B
    Yes
  If the users know about the subnet, should we allow them to pick a random address for the pool of addresses allocated to IIITD
    No, two users may end up assigning the same IP address
  IP assignment?
    A central authority can assign an address to each user
    The central authority will tell the user which IP to use
    The user will configure its machine to use the suggested IP address
    Problem?

## Slide 13: Obtaining host address
Let’s say IIITD got 200.23.16.0/23
  Can we use 200.23.16.1 for user A and 200.23.16.2 for user B
    Yes
  If the users know about the subnet, should we allow them to pick a random address for the pool of addresses allocated to IIITD
    No, two users may end up assigning the same IP address
  IP assignment?
    A central authority can assign an address to each user
    The central authority will tell the user which IP to use
    The user will configure its machine to use the suggested IP address
    Problem?
      Whenever a user moves from one subnet to another, it has to manually configure the IP address
      We need a mechanism to do this automatically

## Slide 14: Obtaining host address
A DHCP server can keep a mapping of all allocated addresses and can lease an IP address on demand
  How can a user talk to the DHCP server?
    How does the user know the IP address of the DHCP server?

## Slide 15: Obtaining host address
A DHCP server can keep a mapping of all allocated addresses and can lease an IP address on demand
  How can a user talk to the DHCP server?
    How does the user know the IP address of the DHCP server?
      It could be fixed
    What if it’s not fixed?

## Slide 16: Obtaining host address
A DHCP server can keep a mapping of all allocated addresses and can lease an IP address on demand
  How can a user talk to the DHCP server?
    How does the user know the IP address of the DHCP server?
      It could be fixed
    What if it’s not fixed?
      broadcast DHCP request
    How does the DHCP server reply to the requesting host? The requesting host doesn’t have an IP yet.

## Slide 17: Obtaining host address
A DHCP server can keep a mapping of all allocated addresses and can lease an IP address on demand
  How can a user talk to the DHCP server?
    How does the user know the IP address of the DHCP server?
      It could be fixed
    What if it’s not fixed?
      broadcast DHCP request
    How does the DHCP server reply to the requesting host? The requesting host doesn’t have an IP yet.
      broadcast DHCP response

## Slide 18: DHCP
Dynamic Host Configuration Protocol (DHCP) is a client-server protocol
One or more DHCP servers are present in the subnet (if not, a relay agent knows the address of the DHCP server)
255.255.255.255 is a broadcast destination address
  We’ll read about broadcasting later in our discussion of the data-link layer

## Slide 19: DHCP
Client sends a DHCP discover message
  UDP DST port: 67, SRC port: 68, DST IP: 255.255.255.255, SRC IP: 0.0.0.0, transaction ID
DHCP servers reply with DHCP offer messages
  DST IP: 255.255.255.255, Proposed IP address, transaction ID, DHCP server ID, Lifetime
  why broadcast?

## Slide 20: DHCP
Client sends a DHCP discover message
  UDP DST port: 67, SRC port: 68, DST IP: 255.255.255.255, SRC IP: 0.0.0.0, transaction ID
DHCP servers reply with DHCP offer messages
  DST IP: 255.255.255.255, Proposed IP address, transaction ID, DHCP server ID, Lifetime
  why broadcast?
    client doesn’t have an IP address yet
Client chooses one response and responds with a DHCP request message
  DST IP: 255.255.255.255, Proposed IP address, transaction ID, DHCP server ID
The server sends a DHCP ACK message to confirm the allocation
  DST IP: 255.255.255.255, Proposed IP address, transaction ID, DHCP server ID, Lifetime

## Slide 21: DHCP
DHCP also provides a mechanism to renew an IP address
  Renewals can use direct messages if the client has a valid IP at the time of renewal

## Slide 22: DHCP
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 23: DHCP
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 24: Network address translation (NAT)
Let’s say IIITD was initially allocated 256 IP addresses
  200.23.16.0/24
After a few years, as the number of intakes increased, it now wants 256 more addresses
How can we assign more addresses to IIITD while keeping the previously assigned addresses and a single subnet mask

## Slide 25: Network address translation (NAT)
Let’s say IIITD was initially allocated 256 IP addresses
  200.23.16.0/24
After a few years, as the number of intakes increased, it now wants 256 more addresses
How can we assign more addresses to IIITD while keeping the previously assigned addresses and a single subnet mask
  assign 200.23.16.0/23
It’s always possible

## Slide 26: Network address translation (NAT)
Let’s say IIITD was initially allocated 256 IP addresses
  200.23.16.0/24
After a few years, as the number of intakes increased, it now wants 256 more addresses
How can we assign more addresses to IIITD while keeping the previously assigned addresses and a single subnet mask
  assign 200.23.16.0/23
It’s always possible
  No, because 200.23.17.0/24 might have been allocated to someone else

## Slide 27: Network address translation (NAT)
NAT allows different organizations to reuse IP addresses
NAT significantly decreases the requirement for unique IP addresses because addresses are shared among organizations
A part of available IP addresses is reserved for private use, such as for NAT
  e.g., 10.0.0.0/8, 192.168.0.0/16

## Slide 28: NAT
How NAT works?
  All traffic of an organization goes via an internal router, say X, which is connected to the public network
    There could be more than one internal router; all of them will work in the same way
  The outgoing interface of X has a public IP address, say 138.76.29.7
  The incoming interfaces of the router have unique private IP addresses
  All devices in the organization have unique private IP addresses
  All devices in the organization can talk to each other via private addresses
    The forwarding is done via switches and internal routers
  All outside communication is done via X

## Slide 29: NAT
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
X
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 30: NAT
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
NAT translation table
public addr private addr
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
4
2
3
X
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 31: NAT send
Let’s say how a device P (IP address: 10.0.0.1) talks to a public server (128.119.40.186:80)
P sends a packet with the following values
  SRC IP: 10.0.0.1 SRC PORT: 3345
  DST IP: 128.119.40.186 DST PORT: 80
X looks at its NAT table for an entry corresponding to 10.0.0.1:3345
  If an entry say 10.0.0.1:3345 → 138.76.29.7:5001 exists
    X overwrites: SRC IP with 138.76.29.7 and SRC PORT with 5001 and forwards the packet
  If 10.0.0.1:3345is not present in the NAT table, and say port 1654 is unused
    X adds 10.0.0.1:3345 →138.76.29.7:1654 to the NAT table
    X overwrites: SRC IP with 138.76.29.7 and SRC PORT with 1654, and forwards the packet

## Slide 32: NAT receive
X receives a packet with DST IP 138.76.29.7 and DST port 5001
X looks for an entry with the target port 5001
  It finds 10.0.0.1:3345 → 138.76.29.7:5001
  NAT replaces the DST IP with 10.0.0.1 and DST port with 3345 and forwards the packet to one of its internal links, depending on the DST IP

## Slide 33: NAT
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
NAT translation table
public addr private addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
X
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 34: Communication between two organizations
Let’s say A and B are two hosts in different organizations, and both of them have IP address 10.0.0.1
How can they talk to each other?

## Slide 35: Communication between two organizations
Let’s say A and B are two hosts in different organizations, and both of them have IP address 10.0.0.1
How can they talk to each other?
Let’s say a server X offered to help them establish the connection

## Slide 36: Communication between two organizations
A
B
X
10.0.0.1
10.0.0.1
178.192.31.65
160.12.45.25
100.100.23.43:80
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 37: Communication between two organization
A sends a message to X with SRC IP: 10.0.0.1 and #port 1234
  NAT maps 10.0.0.1:1234 → 178.192.31.65:9753
B sends a message to X with SRC IP: 10.0.0.1 and #port 2000
  NAT maps 10.0.0.1:2000 → 160.12.45.25:6544
X learns both extremal addresses and shares them
  X sends a message to B with 178.192.31.65:9753 as payload
  X sends a message to A with 160.12.45.25:6544 as payload
B sends a message to A at 178.192.31.65:9753
NAT-enabled router in A’s organization finds 178.192.31.65:9753 → 10.0.0.1:1234 and forwards the message to 10.0.0.1:1234
A receives the message, and verifies the IP address of B 160.12.45.25:6544 in the packet header
A sends a message to 160.12.45.25:6544
NAT-enabled router in B’s organization forwards it to B

## Slide 38: Communication between two organizations
Google STUN servers allow clients behind a NAT to discover their public IP address

## Slide 39: More restrictive NAT
Some versions of NAT are more restrictive
  They use a unique mapping for (SRC IP, SRC PORT, DST IP, DST PORT), which makes it harder for two hosts behind different NATs to communicate with each other

## Slide 40: NAT
Advantages
  Provides anonymity for end users
  Enable reuse of IP addresses, which temporarily solves the problem of the scarcity of available IP addresses
Disadvantage
  Two hosts behind different NATs can’t easily talk to each other
  Breaks the end-to-end argument, which states that all the intelligence should be at the end hosts
  If the payload contains private addresses, they can’t be overwritten by the NAT-enabled router

## Slide 41: IPv6 Header
// Size of the IPv6 header is 40 bytes
struct ipv6hdr {
__u8 traffic_class:4; // traffic class, e.g., voice call
__u8 version:4; // IP version number, 6 for IPv6
__u8 flow_label[3]; // assign priority to flows
__be16 payload_len; // length of the payload, i.e., size of IPv6 datagram - 40
__u8 nexthdr; // same as protocol in IPv4
__u8 hop_limit; // same as TTL in IPv4
__be32 saddr[4]; // 128-bit source IP address
__be32 daddr[4]; // 128-bit destination IP address
};

## Slide 42: IPv6
IPv6 was designed in late 1990s to solve the problem of the possible exhaustion of IPv4 addresses
  IPv6 addresses are 128-bit long
  Now, every grain of sand on the planet is IP addressable
Flow labelling
  IPv6 introduces a flow label field in the header, allowing packets belonging to the same flow to be labeled
  This enables routers to identify and provide special handling (such as QoS or priority scheduling) for specific flows without inspecting transport-layer headers

## Slide 43: IPv6
Fragmentation
  IPv6 does not allow fragmentation and reassembly of packets of sizes greater than MTU, which adds additional overhead at the routers
  Instead, routers drop the datagrams and send a “Packet too Big” ICMP error message to the sender
  Sender resends the data with a smaller IP datagram
Header checksum
  The header checksum is removed in IPv6 because data-link and transport layers also add integrity checks, and recomputing the checksum at the IP layer adds additional overhead

## Slide 44: Interoperability of IPv6 and IPv4
How two IPv6 hosts can talk to each other, when some of the intermediate routers only support IPv4

## Slide 45: Tunneling
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 46: Tunneling
B-to-C:
IPv6 inside
IPv4
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Note source and destination addresses!
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 47: Tunneling
The intervening sets of IPv4 routers between two IPv6 routers is called a tunnel
The sending side of the tunnel encapsulates the IPv6 datagram inside an IPv4 packet
The destination address is the IPv4 address of the receiving end of the tunnel
The routers in the tunnel forward the packet as usual, unaware of the fact that the packet actually contains an IPv6 datagram
The receiving end of the tunnel retrieves the IPv6 datagram from the packet and forwards the IPv6 datagram to the next hop

## Slide 48: Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 49: IPv6 deployment status
Complete migration to IPv6 is still very much a work in progress
  Migration started in early 2000s
  As of October 2025, around 45-49% of the global internet traffic uses IPv6
    https://en.wikipedia.org/wiki/IPv6_deployment