## Slide 2: Today’s topics
Routing protocols
Link state routing
Distance vector routing

## Slide 3: References
Read Chapter-5.2 from the Kurose and Ross
Read Chapter-3.4 from the Peterson and Davie

## Slide 4: Forwarding table
The forwarding table is populated in two ways
Distributed approach (traditional networks)
  All routers collaborate to compute their own forwarding tables
Centralized approach (software-defined networking, SDN)
  A central controller computes the forwarding tables for all routers and pushes them to the routers

## Slide 5: Interconnection of routers
u
y
x
w
v
z
50 Mbps
50 Mbps
100 Mbps
30 Mbps
100 Mbps
100 Mbps
50 Mbps
20 Mbps
30 Mbps
20 Mbps
mobile network
mobile network
200.23.16.0/26
200.23.18.0/23
200.24.0.0/16
100.23.25.0/24
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 6: Cost of a link
.

## Slide 7: Cost of a link
The cost of a link could be the inverse of bandwidth, link delay, the amount of traffic on the link, or defined by a network operator, etc.

## Slide 8: Reliable flooding

## Slide 9: Reliable flooding
Each router sends its link-state information to all other routers via reliable flooding
The link-state information is stored in a link-state packet (LSP)

## Slide 10: Link-state packet (LSP)
The LSP of router A contains
sequence number
If the next hop is router B
  ID of B
  IP address A’s network interface connected to B
  the cost of the outgoing link
If the next hop is an end user’s or an organization's network
  network prefix and subnet mask of the A’s interface that connects to the network

## Slide 11: Reliable flooding
Each router reliably (i.e., using acknowledgments) sends LSPs to its neighbors
Neighbors check if they already have a stored version of the LSP
  If the sequence number is larger than the stored one
    they replace the old version with the new one and reliably forward the packet to all neighbors except the one from which they received the packet
  Otherwise, the LSP is discarded
This ensures that eventually all routers will receive LSP from all other routers

## Slide 12: Reliable flooding
Goal
  Newest information must propagate as quickly as possible, whereas the old information must be removed and should not propagate

## Slide 13: Change in topology

## Slide 14: Change in topology
The routers periodically send ping messages to neighbors to detect link or router failures
If a router goes down, its neighbors start reliable flooding to propagate the change in topology
The routers compute their forwarding table again if they encounter a change in the topology

## Slide 15: Change in topology
When the router is up again, it requests LSPs from neighboring routers, stores them, and shares its own LSPs with neighboring nodes using reliable flooding to inform all routers about the change in topology
The routers compute their forwarding table again if they encounter a change in the topology

## Slide 16: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y

## Slide 17: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
0
1
6
4
2
7
9
3
2
5
10
t
x
z
y
s
t
x
z
y
0

## Slide 18: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
0
1
6
4
2
7
9
3
2
5
10
t
x
z
y
s
t
x
z
y
0
We can also use gravity to find the shortest path. Let’s say vertices are some solid objects. If we connect the adjacent objects using a thread of length equal to the weight of the corresponding edge and hang the source object to a hook in the ceiling, then the order in which the objects will appear from top the bottom, would be the order in which we are going to compute the shortest path. All the threads that are not loose are on the shortest path. We also need to remove the threads that are going in the upward direction.

## Slide 19: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y

## Slide 20: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Initialization:
N’ = {u}
for all nodes v
if v is a neighbour of u
then D(v) = c(u, v)
else D(v) =
The next node that appears due to gravity must be directly connected to s.
y will appear next, because it has the shortest distance among all nodes directly connected to s.
White nodes are in N’
The values in the circles represent D(v)

## Slide 21: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
The next node that appears next due to gravity must be directly connected to s or y.
Update distances from y.

## Slide 22: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
After updating distances from y.
The node that appears next must be directly connected to s or y
It’s z, because z has the shortest distance.

## Slide 23: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
The next node that appears due to gravity must be directly connected to s, y, or z.
Update distances from z.

## Slide 24: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
After updating distances from z.
The node that appears next must be directly connected to s, y, or z.
It’s t, because t has the shortest distance.

## Slide 25: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
The next node that appears due to gravity must be directly connected to s, y, z, or t.
Update distances from t.
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N

## Slide 26: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
After updating distances from t.
The node that appears next must be directly connected to s, y, z, t
It’s x, because we have no other option.

## Slide 27: Shortest Path
0
1
6
4
2
7
9
3
2
5
10
s
t
x
z
y
Loop
find w not in N’ such that D(w) is minimum
add w to N’
update D(v) for each neighbour v of w and not in N’:
D(v) = min(D(v), D(w) + c(w, v))
until N’ = N
All the nodes are in N’. The algorithm terminates.

## Slide 28: Time complexity
In the simplest implementation, when we find the minimum using a linear search, let V and E be the number of vertices and edges
First iteration V
Second iteration V-1
Third iteration V-2
and so on
To update the weights of the neighbours, we traverse all edges overall
Time complexity:
V + (V - 1) + (V-2) + … + 1 + E O()

## Slide 29: Time complexity
Using min-heap:

## Slide 30: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 31: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 32: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
4,x
∞
2,x
2,u
ux
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 33: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
4,x
∞
2,x
2,u
ux
3,y
4,y
2,u
uxy
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 34: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
4,x
∞
2,x
2,u
ux
3,y
4,y
2,u
uxy
3,y
4,y
uxyv
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 35: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
4,x
∞
2,x
2,u
ux
3,y
4,y
2,u
uxy
3,y
4,y
uxyv
4,y
uxyvw
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 36: Link-state routing (example)
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
D(v) is the distance of v from the source, which is known at this stage of the algorithm
p(v) is the immediate predecessor of v on the path to v with distance D(v)
means the path is unknown at this stage of the algorithm
4,x
∞
2,x
2,u
ux
3,y
4,y
2,u
uxy
3,y
4,y
uxyv
4,y
uxyvw
uxyvwz
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 37: Link-state routing (Exercise)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 38: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 39: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
1
uw
∞
11,w
6,w
5,u
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 40: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
1
uw
∞
11,w
6,w
5,u
2
uwx
14,x
11,w
6,w
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 41: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
1
uw
∞
11,w
6,w
5,u
2
uwx
14,x
11,w
6,w
3
uwxv
14,x
10,v
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 42: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
1
uw
∞
11,w
6,w
5,u
2
uwx
14,x
11,w
6,w
3
uwxv
14,x
10,v
4
uwxvy
12,y
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 43: Link-state routing (example)
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
1
uw
∞
11,w
6,w
5,u
2
uwx
14,x
11,w
6,w
3
uwxv
14,x
10,v
4
uwxvy
12,y
4
uwxvyz
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 44: Oscillations
Let’s use the load on a link as its cost. Edge labels are the current load. Nodes , , and are sending data at a constant rate of , 1, 1 Mbps to .
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
What will be the shortest paths if we run the link-state routing protocol at this point?
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 45: Oscillations
Let’s use the load on a link as its cost. Edge labels are the current load. Nodes , , and are sending data at a constant rate of , 1, 1 Mbps to .
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 46: Oscillations
Let’s use the load on a link as its cost. Edge labels are the current load. Nodes , , and are sending data at a constant rate of , 1, 1 Mbps to .
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
e
1
1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 47: Oscillations
Let’s use the load on a link as its cost. Edge labels are the current load. Nodes , , and are sending data at a constant rate of , 1, 1 Mbps to .
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
e
1
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
e
1
1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 48: Oscillations
Let’s use the load on a link as its cost. Edge labels are the current load. Nodes , , and are sending data at a constant rate of , 1, 1 Mbps to .
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
e
1
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
e
1
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
e
1
1
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 49: Oscillations
How to prevent oscillations?

## Slide 50: Oscillations
How to prevent oscillations?
  Don’t use the current load as the cost of a link
    Undesirable: the goal of routing to find efficient (uncongested) routes
    Instead of using the instantaneous load, the average load over a period of time could be a better metric
  It turns out that if routers advertise their link-state at random times and all nodes don’t run the routing algorithms at the same time, this oscillation can be reduced
  Additionally, network operators can assign costs to different links to achieve better load balancing