## Slide 2: Today’s topics
Assignment-1
Cookies
Web caching

## Slide 3: References
Chapter 2.2.4 and 2.2.5 from the Kurose and Ross

## Slide 4: Assignment-1
Simulating packet drop using the E1000 network driver

## Slide 5: Big-endian and Little-endian
Big-endian: Store the most significant byte first in the memory. Little-endian: Store the least significant byte first in the memory.
For example, let’s say we want to store a 4-byte word 0xab12cd87 at location 0x1000.

## Slide 6: Big-endian and Little-endian
For example, let’s say we want to store a 4-byte word 0xab12cd87 at location 0x1000.
In Big-endian: 0xab will be stored at 0x1000. 0x12 will be stored at 0x1001. 0xcd will be stored at 0x1002. 0x87 will be stored at 0x1003.

## Slide 7: Big-endian and Little-endian
For example, let’s say we want to store a 4-byte word 0xab12cd87 at location 0x1000.
In Little-endian: 0x87 will be stored at 0x1000. 0xcd will be stored at 0x1001. 0x12 will be stored at 0x1002. 0xab will be stored at 0x1003.

## Slide 8: Byte order
On an Intel CPU, the data is stored in the Little-endian format.
In network headers, the data is stored in Big-endian format, often called network byte order.

## Slide 9: IP address
Convert the following IP address to a 32-bit hexadecimal value
  7.8.9.3
How will it be stored in a network header?

## Slide 10: IP address
Convert the following IP address to a 32-bit hexadecimal value
  7.8.9.3
  0x07080903
How will it be stored in a network header?
  0x03090807

## Slide 11: Packet structure

## Slide 12: Data-link layer header (14 bytes)
struct ethhdr { unsigned char h_dest[6]; // destination mac address unsigned char h_source[6]; // source mac address __be16 h_proto; // 2-byte protocol };
__be16: two-byte value stored in Big-endian format

## Slide 13: Network layer header (minimum 20 bytes)
struct iphdr { __u8 ihl:4; // length of header = ihl * 4 __u8 version:4; // 4-bit version __u8 tos; __be16 tot_len; // Entire packet size, header + data __be16 id; __be16 frag_off; __u8 ttl; // Hop limit, decremented at each hop __u8 protocol; // protocol TCP=6, UDP=17 __sum16 check; // header checksum __be32 saddr; // source IP address __be32 daddr; // destination IP address char options[]; // variable length };

## Slide 14: UDP header (8 bytes)
struct udphdr { __be16 source; // source port __be16 dest; // destination port __be16 len; // length of UDP header + data __sum16 check; // checksum of UDP header, payload, part of IP header };

## Slide 15: TCP header (minimum 20 bytes)
struct tcphdr { __be16 source; // source port __be16 dest; // destination port __be32 seq; // sequence number __be32 ack_seq; // acknowledgement number __u16 ae:1; __u16 res1:1; __u16 doff:4; // Length of TCP header = doff * 4 __u16 fin:1; __u16 syn:1; // start connection __u16 rst:1; __u16 psh:1; __u16 ack:1; // acknowledgment valid __u16 urg:1; __u16 ece:1; __u16 cwr:1; __be16 window; // window size __sum16 check; // checksum of TCP header, data, part of IP header __be16 urg_ptr; char options[]; // variable length };

## Slide 16
facilitates easy access to different headers in a packet
various useful fields to access the headers, such as
  points to the link-layer header
  points to the network-layer header
  points to the transport-layer header
Other useful routines that take a as input
  returns a pointer of type
  returns a pointer of type
  returns a pointer of type
  returns a pointer of type

## Slide 17: Useful routines
e1000_xmit_frame
  takes an argument skb of type struct sk_buff
  skb contains pointers to the various headers of the actual packet
  updates an available descriptor in the transmit ring with the physical address of the packet
  updates the TDT register, which allows the NIC to transmit the packet
e1000_clean_tx_irq
  part of the interrupt handling for sending packets
  Once the packet has been sent, the NIC sends an interrupt
  Notes that the transmit descriptors can now be available for future transmits
  May also free the buffers used for the sent packets.

## Slide 18: User tools
server: A TCP server that receives data from the client
client: A TCP client that sends data to the server
  Takes the IP address of the server as input
block: An application that instructs the driver to drop future packets to a given destination at a given rate
  ./block 172.32.89.10 20
    Drop 10% packets with destination IP address = 172.32.89.10
  The block application creates a UDP packet with a 5-byte payload.
    The first four bytes are 172, 32, 89, 10, i.e., the IP address
    The fifth byte is 20, i.e., the drop rate

## Slide 19: Implementation
Monitor all ongoing packets
  If the destination IP address is 100.100.100.100, record the IP address and drop rate from the payload
  If the IP address matches the blocking IP address, drop packets with the given rate
    Notice that after dropping a packet, you may need to release the buffer
    Look at the interrupt handler for better clarity
  Only one IP can be registered for dropping packets
    ./block 192.1.3.4 10
      dropping 10% packets to 192.1.3.4
    ./block 123.43.24.52 1
      192.1.3.4 is unblocked, i.e., no dropping
      dropping 1% packets to 192.1.3.4
    ./block 123.43.24.52 5
      Now dropping with 5% probability

## Slide 20: Test you implementation
Start server on host using ./server
Drop 5% packets to the host
  ./block 192.3.5.6 5
    Replace 192.3.5.6 with the IP address of your host.
Run client inside the VM
  ./client 192.3.5.6
    Replace 192.3.5.6 with the IP address of your host.
If everything works perfectly, the TCP protocol should be able to handle the packet loss
  The server will print “100001 packets received in ... milliseconds”

## Slide 21: Monitor retransmission
Monitor retransmission by the TCP protocol before and after the invocation of the client
  netstat -s | grep retransmitted

## Slide 22: Block websites
Ping Google using
  ping www.google.com
  Block all packets to Google using ./block 172.34.54.65 100
    Replace 172.34.54.65 with the actual IP address of Google
  The ping www.google.com should not work now

## Slide 23: Compiling and using the E1000 device driver
Compile the E1000 driver using
  make M=drivers/net/ethernet/intel/e1000
Copy linux-6.16/drivers/net/ethernet/intel/e1000/e1000.ko to your VM
Reload the driver
  sudo modprobe -r e1000 followed by sudo insmod e1000.ko

## Slide 24: Submission
Implement everything in e1000_main.c
Report various statistics for different drop rates as mentioned in the assignment
Ask any queries related to the assignment after the class or during office hours

## Slide 25: Cookies

## Slide 26: Cookies
HTTP, being a stateless protocol, sometimes may not be the best thing for both users and the server hosting a website
  For example, the server may want to show the relevant content based on their previous browsing sessions, e.g., YouTube, Amazon
How can we solve the problem?

## Slide 27: Cookies
HTTP, being a stateless protocol, sometimes may not be the best thing for both users and the server hosting a website
  For example, the server may want to show the relevant content based on their previous browsing sessions, e.g., YouTube, Amazon
How can we solve the problem?
  Ask users to authenticate every time
    Might not be the best policy. Users may not want to share their private information.

## Slide 28: Cookies
HTTP is stateless
  Each request is independent; the server doesn’t remember previous requests.
  Problem: Personalized content (shopping history, recommendations) becomes difficult.
How can we solve the problem?
  Ask user to authenticate every time
    inconvenient for users.
  Ask browsers to save an identifier suggested by the website
  For subsequent visits, the browser sends the identifier along with the URL
  The website looks into its database, finds metadata corresponding to the user, and customizes content
  For example, if the user has searched for shoes previously, the website can suggest catchy shoes that might tempt the user to buy them.

## Slide 29: Cookies
When a user visits a website, say amazon, the first time it creates an ID, say 1678, for the user and adds a line called Set-Cookie 1678 in its response
The browser saves amazon: 1678 in its cookie file. The cookie file may have other entries, such as ebay: 8734
For subsequent requests to amazon, the browser adds a line cookie: 1678 in its request
The amazon keeps a mapping ``1678 → user’’ data in its backend
If the user visits again after a week, the browser again sends cookie: 1678 in its request, allowing amazon to send a customized response to the user

## Slide 30: Cookies

## Slide 31: Cookies
Amazon server
usual HTTP response msg
usual HTTP response msg
cookie file
one week later:
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual HTTP request msg
Amazon server
creates ID
1678 for user
create
entry
usual HTTP response
set-cookie: 1678
ebay 8734
amazon 1678
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database
time
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 32: Cookies
Cookies can also be used for authentication
When first-time users log in to a website, the server creates a cookie for the user
For subsequent visits, users don’t need to log in again; instead, the server can authenticate the user based on the cookie provided by the browser

## Slide 33: Cookies
Issues?

## Slide 34: Cookies
Cookies are controversial because they can invade a user’s privacy.
The Digital Personal Data Protection (DPDP) Act in India prevents websites from collecting personal data without the user’s explicit consent.

## Slide 35: Performance
Suppose a popular website is hosted in the US, e.g., Netflix
It gets a lot of traffic from all over the world
In addition to the website servers, due to the high demand across the globe, gateways all over the world may get overloaded
How can we reduce the load on the website and the intermediate gateways?

## Slide 36: Web caching

## Slide 37: Web caching
A web cache (proxy server) is used as a cache for the original server
Each request is forwarded to a web cache
If a local copy is present on the web cache, it is served to the client
Otherwise, the web cache obtains a copy from the server, saves it in its local storage, and sends it back to the client

## Slide 38: Web caching
client
Web
cache
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
HTTP response
HTTP response
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 39: Web caching
There can be more than one web cache
Web caches are placed strategically to reduce the load on gateways in the network core
A client’s requests are forwarded to the nearest web cache

## Slide 40: Example
Machines in the institutional network are clients
Clients connected to gateway B via 100 Mbps links
Gateway B to the public internet using a 15 Mbps link
Servers are connected to A using a 100 Mbps link
Average object size = 1 Mb
Average request rate = 1 request/second
RTT = 2 seconds
Request size: 1 Kb
Packet size: 1 Kb
How long will it take for C to receive a response from D
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 41: Example
Average object size = 1 Mb
Average request rate = 1 request/second
RTT = 2 seconds
Request size: 1 Kb
Packet size: 1 Kb
How long will it take for C to receive a response from D
Connection time: 2 seconds
Request transmission delay = (1 Kb/100Mb) + (1Kb/15Mb) + (1Kb/100Mb)
Delay between request and response = 2 seconds
Response transmission time (1Mb/15Mb)
Total time = 2 s + 0.087 ms + 2 s + 66.67 ms 4s
Therefore, RTT is the major factor in the total time.
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 42: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
Does the RTT remain the same?
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 43: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
Does the RTT remain the same?
No, the traffic intensity at router A during the return path is: 1
As the traffic intensity reaches one, the queuing delay rises sharply
RRT could be of the order of minutes
How can we fix this problem?
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 44: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
Does the RTT remain the same?
No, the traffic intensity at router A during the return path is: 1
As the traffic intensity reaches one, the queuing delay rises sharply
RRT could be of the order of minutes
How can we fix this problem?
Upgrade the network link between A and B to 100 Mbps
origin
servers
public
Internet
institutional
network
100 Mbps
100 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 45: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
After upgrading the network link between A and B to 100 Mbps
Will the RTT still increase after this upgrade?
origin
servers
public
Internet
institutional
network
100 Mbps
100 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 46: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
After upgrading the network link between A and B to 100 Mbps
Will the RTT still increase after this upgrade?
No, the traffic intensity at A is 0.15, which is low.
Upgrading the bandwidth of links in the network core could be very expensive.
Any other option?
origin
servers
public
Internet
institutional
network
100 Mbps
100 Mbps
100 Mbps
A
B
C
D
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 47: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
Upgrading the bandwidth of links in the network core could be very expensive.
Any other option?
Install a web cache in the institutional network
If the Hit rate of the web cache is 40%.
Will the RRT increase?
Traffic intensity at
Traffic intensity at
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
1 Gbps LAN
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 48: Example
Let’s say the average request rate increased to 15 requests / second
Average object size = 1 Mb
Average request rate = 15 requests / second
Request size: 1 Kb
Packet size: 1 Kb
Upgrading the bandwidth of links in the network core could be very expensive.
Any other option?
Install a web cache in the institutional network
If the Hit rate of the web cache is 40%.
Will the RRT increase?
Traffic intensity at = 0.6
Traffic intensity at = 0.15 (assuming all traffic goes to C)
A traffic intensity of less than 0.8 typically corresponds to a small delay.
origin
servers
public
Internet
institutional
network
100 Mbps
15 Mbps
100 Mbps
A
B
C
D
1 Gbps LAN
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 49: Web caches
Web caches play an important role in reducing end-to-end latency to your popular streaming website, such as YouTube and Netflix

## Slide 50: Web caches
Problem with web caches

## Slide 51: Web caches
Problem with web caches
  The copy in the web cache could be stale

## Slide 52: Conditional GET
An HTTP response message contains the Last-Modified field
  It indicates the last time this page was modified
It also has a Cache-Control field that controls how long the webpage can be cached, without checking the server
  e.g., max-age=2049, means that the webpage can be cached for 2049 seconds
HTTP/1.1 200 OK
Content-Type: text/html
ETag: "84238dfc8092e5d9c0dac8ef93371a07:1736799080.121134"
Last-Modified: Mon, 13 Jan 2025 20:11:20 GMT
Cache-Control: max-age=2049
Date: Sun, 17 Aug 2025 13:02:20 GMT
Content-Length: 1256

## Slide 53: Conditional GET
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 54: Conditional GET
After the page has expired, the web cache issues a conditional GET request to the server
The conditional GET request contains the following line
  If-Modified-since: Mon, 13 Jan 2025 20:11:20 GMT
  (Notice, the timestamp is the same as the last modification timestamp in the cached response)
If the webpage was not modified, the server responds with:
  HTTP/1.1 304 Not Modified
  The actual object is not included in the response
  However, the response may contain new Cache-Control instructions to extend the lifetime of the cached response