## Slide 2: Today’s topics
Domain name system (DNS)
Peer-to-peer (P2P) file distribution

## Slide 3: DNS message format
Both request and reply have the same format
The question section contains the name and the type of the query
The answer contains the resource records for the name that was originally queried
The authority section contains the record of other authoritative servers
The additional section contains other useful information
  e.g., the answer field contains the canonical name and the additional section contains type A record for the canonical name
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 4: DNS example
root servers:
  https://www.iana.org/domains/root/servers
  a.root-servers.net 198.41.0.4
  b.root-servers.net 170.247.170.2
  etc.
dig @198.41.0.4 www.example.com
dig is a DNS lookup tool.

## Slide 5: Inserting records
The records are inserted by registrars, e.g., www.godaddy.com
  Registrar verifies the uniqueness of the domain name
  enter the new domain name in its database
  You may also provide the name and IP address of your authoritative DNS server; the registrar will add it to the corresponding TLD servers

## Slide 6: Inserting records
Let’s you want to register a new website networkguy.com
You also created an authoritative DNS server dns1.networkguy.com with the IP address 121.23.43.54
What needs to be done in order to allow users to find the IP address of your website?

## Slide 7: Inserting records
Let’s you want to register a new website networkguy.com
You also created an authoritative DNS server dns1.networkguy.com with the IP address 121.23.43.54
What needs to be done in order to allow users to find the IP address of your website?
  .com TLD servers must have an entry for your authoritative DNS server

## Slide 8: Inserting records
Let’s you want to register a new website networkguy.com
You also created an authoritative DNS server dns1.networkguy.com with the IP address 121.23.43.54
The registrar will add the following entries to the .com TLD servers
  (networkguy.com, dns1.networkguy.com, NS)
  (dns1.networkguy.com, 121.23.43.54, A)
When a local DNS server tries to find the IP address of www.networkguy.com it will receive the following response from the TLD server
  (networkguy.com, dns1.networkguy.com, NS)
  (dns1.networkguy.com, 121.23.43.54, A)
Afterward, the local DNS server will send a query to 121.23.43.54 to get the address of www.networkguy.com

## Slide 9: DNS vulnerabilities
DNS spoofing
  Can you guess what it might be?

## Slide 10: DNS vulnerabilities
DNS spoofing
  An attacker sends a lot of requests to the DNS server to keep it busy
  Before the DNS server could reply to the victim, the attacker sends a fake response to the requesting host, impersonating itself as the DNS server
  The victim fetches the attacker’s chosen IP from the response and starts talking to the wrong website, which may steal sensitive information from the user
We’ll discuss later how these attacks can be prevented

## Slide 11: DNS homework
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
// DNS header
struct dns_header {
__be16 id;
__be16 flags;
__be16 num_ques; // # questions
__be16 num_ans; // # answer RRs
__be16 num_auth; // # authority RRs
__be16 num_add; // # additional RRs
};
struct dns_q {
__be16 type;
__be16 class;
};
struct dns_rr {
__be16 type;
__be16 class;
__be32 ttl;
__be16 rlen;
unsigned char rdata[];
};
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 12: DNS homework
The port number of a DNS server is 53
If the source/destination port address in a UDP packet is 53, it means that it could be a DNS request/response message
The question section starts just after the DNS header

## Slide 13: DNS homework
Each entry in the question section starts with a followed by an element of type struct dns_q
Each entry in the other sections (answers, authority, additional) starts with a followed by an element of type struct dns_rr

## Slide 14: Compressing names
dig @198.41.0.4 www.example.com

## Slide 15: Storing
The is stored in a compressed format
Let’s say there are three names in a DNS record:
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.

## Slide 16: Storing name
Without compression
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.
1 | l | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
1 | j | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
6 | g | t | l | d | - | s | 3 | n | e | t | 0 |  | 
The is divided into labels. i.e., the substring separated by dots.
Labels are stored in the DNS message.
The length of the label is stored before storing the actual labels.
An empty label, i.e., a label of length zero, is stored at the end of the name.
total bytes required to store all three strings =

## Slide 17: Storing name
Without compression
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.
1 | l | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
1 | j | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
6 | g | t | l | d | - | s | 3 | n | e | t | 0 |  | 
The is divided into labels. i.e., the substring separated by dots.
Labels are stored in the DNS message.
The length of the label is stored before storing the actual labels.
An empty label, i.e., a label of length zero, is stored at the end of the name.
total bytes required to store all three strings = 40 bytes

## Slide 18: Storing name
Start offset of the first name w.r.t. the starting address of the DNS message is 0x10
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.
1 | l | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
1 | j |  |  |  |  |  |  |  |  |  |  |  | 
htons(0x12)
The is divided into labels. i.e., the substring separated by dots.
If the remaining labels have already been stored at offset X, store the 2-byte X in Big-endian format.
total bytes required to store all three strings =
htons(0x12)

## Slide 19: Storing name
Start offset of the first name w.r.t. the starting address of the DNS message is 0x10
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.
1 | l | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
1 | j |  |  |  |  |  |  |  |  |  |  |  | 
htons(0x12)
The is divided into labels. i.e., the substring separated by dots.
If the remaining labels have already been stored at offset X, store the 2-byte X in Big-endian format.
total bytes required to store all three strings = 20 bytes
Problem?
htons(0x12)

## Slide 20: Storing name
How do we know if the first byte of a name corresponds to the length of a label or the offset of the string with respect to the starting address of the DNS record (i.e., the address of the DNS header)
  Restrict the maximum length of a label to 63
  Restrict the maximum offset to 14 bits
  If the top two bits in the first two bytes are one, then the remaining 14 bits are offset; otherwise, the first byte is the length of the label stored in the next bytes
  Why does this work?

## Slide 21: Storing name
How do we know if the first byte of a name corresponds to the length of a label or the offset of the string with respect to the starting address of the DNS record (i.e., the address of the DNS header)
  Restrict the maximum length of a label to 63
  Restrict the maximum offset to 14 bits
  If the top two bits in the first two bytes are one, then the remaining 14 bits are offset; otherwise, the first byte is the length of the label stored in the next bytes
  Why does this work?
    Because the maximum length of a label is 63, it can fit into 6 bits

## Slide 22: Storing name
Start offset of the first name w.r.t. the starting address of the DNS message is 0x10
l.gtld-s.net.
j.gtld-s.net.
gtld-s.net.
1 | l | 6 | g | t | l | d | - | s | 3 | n | e | t | 0
1 | j |  |  |  |  |  |  |  |  |  |  |  | 
htons(0xc012)
htons(0xc012)
The name is divided into labels. i.e., the substring separated by dots.
If the remaining substring has already been stored at offset X, store 2-byte (X | 0xc000) in Big-endian format.
Total bytes required to store all three strings = 20 bytes

## Slide 23: How to read name
// read offset
unsigned short off = ntohs(*((__be16*)buf));
if ((off >> 14) == 3) {
// string is stored at the offset, (off & 0x3FFF)
// record header starts at ((char*)buf) + 2
}
else {
// length of the next label is len = buf[0]
// if the len is zero, the next byte corresponds to the record header
// After reading len bytes corresponding to label, advance buf and goto line 1
}

## Slide 24: rdata
The value of a resource record is stored in a variable-length byte array called rdata
The length of the rdata is rlen
Depending on the type, the length of the rdata varies
  e.g., for a type-A record, it would be a 32-bit IP address
  for type CNAME, it would be a name
  etc.
In the homework, you need to skip the rdata to find the address of the next record

## Slide 25: Peer-to-peer (P2P) file distribution

## Slide 26: Peer-to-peer (P2P) file distribution
Unlike the client-server mode in the peer-to-peer model, each client plays the role of both client and server
  i.e., a client downloads part of the file from some clients and uploads the already downloaded parts to some clients who don’t have them

## Slide 27: File distribution
us
uN
dN
server
network (with abundant
bandwidth)
file, size F
us: server upload capacity
ui: peer i upload capacity
di: peer i download capacity
u2
d2
u1
d1
di
ui
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 28: File distribution in client-server architecture
The server distributes a file of size F bits
N clients
The upload speed of the server is bits/second
The download speed of the clients
The bandwidth of the network core is very high, i.e., the bottleneck links are the links connecting the server and clients to the network core
What is the minimum total distribution time?
  The distribution time is the time required to distribute N copies to each client.

## Slide 29: File distribution in client-server architecture
N clients
The upload speed of the server is bits/second
The download speed of the clients
Minimum total distribution time >=

## Slide 30: File distribution in client-server architecture
N clients
The upload speed of the server is bits/second
The download speed of the clients
Total distribution time >= max {}
The total distribution time increases linearly with the number of clients.

## Slide 31: File distribution in P2P architecture
N clients
The upload speed of the server is bits/second
The upload speed of the clients
The download speed of the clients
Total distribution time >=

## Slide 32: File distribution in P2P architecture
N clients
The upload speed of the server is bits/second
The upload speed of the clients
The download speed of the clients
Total distribution time >= max{ , }
Because the upload speed also increases linearly with the number of clients, the total distribution time is non-linear.

## Slide 33: File distribution in P2P architecture
= u
= 10u
(a peer can transmit the entire file in one hour)
The distribution time is less than an hour, irrespective of the number of peers in the P2P architecture.
The distribution time increases linearly with the number of peers in the client-server architecture.
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 34: BitTorrent
A collection of peers (called torrent) distribute a particular file
File is divided into equal size chunks, peers download chunks from each other
When a peer first joins a torrent it has no chunks. Once it accumulates some chunks it also uploads the downloaded chunks to other peers
A peer may leave or join at any time
A peer may choose to upload chunks even after acquiring the file

## Slide 35: BitTorrent
How will you design something like BitTorrent?

## Slide 36: BitTorrent
Each torrent has an infrastructure node called a tracker (kind of a server)
When a peer (say Alice) joins, she registers herself with the tracker
The tracker randomly selects a list of peers, say 50 peers, and sends it to Alice
Alice tries to establish a TCP connection with those peers. The successful connections, say 10, are called neighbours

## Slide 37: BitTorrent
Alice obtains the list of chunks from the neighbors, and requests first for the rarest chunks (the chunks that are rarest among the neighbors)
  The idea is to roughly equalize the number of copies of the chunks
For uploading data, Alice picks four users who are supplying her data at the highest rate, called tit-for-tat trading
  called the unchoked peers
  The download rates are recalculated every 30 seconds
She also picks one random neighbor, say Bob, after every 30 seconds, in addition to the prioritized peers
  Bob is called optimistically unchoked
  This scheme allows new peers to receive data
  Bob can become an unchoked peer by sending data to Alice at a high rate
All other peers are choked, and they don’t receive anything from Alice