## Slide 2: Reference
Chapter-3 from Intel Manual Vol-3

## Slide 3: Example
Firefox invokes receive(buf) system call to receive a packet in the buf
  receive(buf) waits until a packet is received in buf
Notes: A user application does the receive system call to receive a packet in buf.

## Slide 4: receive
#define RX_STATUS_PORT 0x402
#define RX_ADDR_PORT 0x403
struct list *wait_list;
void receive (char *buf) {
/* configure device to copy packet
* to buf when it is received
*/
outl (RX_ADDR_PORT, buf);
outl (RX_STATUS_PORT, 0);
thread_block(wait_list); // put the current thread to wait_list and schedule a new thread
}
Notes: The receive system call handler is a device driver. A device driver is a piece of code that talks to a particular device. In this case, the device driver configures the network device to copy the packet into buf (using DMA), when a packet is received. The current thread is blocked, and a new thread is scheduled.

## Slide 5: Interrupt
rx_intr is invoked after the device has copied an incoming packet to buf
void rx_intr () {
thread_unblock(wait_list); // remove a thread from wait_list
// and put it to the ready list
}
Notes: After the device has copied an incoming packet to buf, it sends an interrupt to the CPU. After receiving the interrupt, the CPU jumps to the interrupt handler of the network device. In the interrupt handler, the thread which is waiting for receiving a packet is moved to the ready list.

## Slide 6: Polling
rx_poll is invoked after every timer interrupt
#define RX_STATUS_PORT 0x402
void rx_poll() {
if (inl(RX_STATUS_PORT) == 1) // if the device has copied a packet to buf
{
thread_unblock(wait_list); // remove a thread from wait_list
// and put it to the ready list
} }
Notes: Alternatively, the CPU can disable interrupts from the network device and check the status of the device (using port I/O or MMIO). In this example, the device sets the status to 1, after copying the packet. If CPU finds that the device status is 1, it moves the thread that was blocked in the receive system call to the ready list.

## Slide 7: Receive livelock
if the packets are received at a very fast rate
  CPU spends most of its time in processing the interrupt handler
  The application (consumer of the packets) won’t get a chance to run
  The throughput of the system will drop to zero
  this situation is called receive livelock

## Slide 8: Eliminating livelock
Use interrupts to initiate polling
Disable interrupts (from the network device) after receiving an interrupt
Re-enabling interrupts after no work is pending

## Slide 9: Extra reading (optional)
Eliminating Receive Livelock in an Interrupt-driven Kernel

## Slide 10: Disk driver
Read disk driver section from chapter 3 of xv6-book for a real device driver
  Will discuss later in this course

## Slide 11: Memory isolation
Processes have their own reserved quota of RAM
Decided by OS during fork/exec
One process can’t access memory of the other processes
OS can access the memory of all processes
Notes: Let’s talk about memory isolation. One of the goals of the OS is to ensure that a process can’t read or write the data of other processes.

## Slide 12: Memory isolation
Memory isolation is done using additional hardware called memory management unit (MMU)
OS expose a different abstraction to the processes for accessing memory called virtual address space
  processes can not access the physical address space directly
MMU translates a virtual address to the corresponding physical address

## Slide 13: Memory isolation
The OS creates the virtual address to physical address mapping
When the MMU is active memory can only be accessed using virtual addresses

## Slide 14: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
Notes: When the MMU is active, all memory accesses are done using virtual addresses. A virtual address is converted to the physical address by the MMU hardware.

## Slide 15: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
1 | 8
2 | 7
3 | 18
4 | 12
OS creates VA to PA mapping.
Notes: There are several ways to implement the virtual address (VA) to physical address (PA) translation. A simple strategy would be that MMU hardware uses a table called MMU table that contains VA to PA mapping. Whenever memory is accessed, the corresponding address is translated into PA using the MMU table. OS is allowed to add or modify entries to this table.

## Slide 16: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
1 | 8
2 | 7
3 | 18
4 | 12
CPU reads from VA:1
DATA will be read from PA:8

## Slide 17: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
1 | 8
2 | 7
3 | 18
4 | 12
CPU reads from VA:1
DATA will be read from PA:8
OS can also modify the existing VA-PA mapping

## Slide 18: Memory isolation
How to implement memory isolation using MMU

## Slide 19: Memory isolation
How to implement memory isolation using MMU
  Create different VA to PA mappings for different processes
Notes: The OS creates different VA-PA mappings for each process.

## Slide 20: schedule
struct thread *ready_list;
struct thread *cur_thread;
void schedule() {
struct thread *prev = cur_thread;
struct thread *next = pop_front(ready_list);
cur_thread = next;
update_mmu_mappings(next);
context_switch(prev, next);
}
Notes: During scheduling, the MMU table is overwritten by the VA-PA mappings corresponding to the target process.

## Slide 21: MMU
Can two processes have the same virtual addresses?

## Slide 22: MMU
Can two processes have the same virtual addresses?
  Yes, as long as the VA-PA mapping is different for both processes, and they are reflected in the MMU table during scheduling

## Slide 23: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
1 | 8
2 | 7
3 | 18
4 | 12
What is the problem with this scheme?
The table could be very large. Where to store this table.

## Slide 24: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
 | base | limit | 
 | 1000 | 256 | 
assert(VA < limit);
PA = VA + base
Notes: An alternative solution to allocate contiguous memory region for a process in the physical address space. The OS decides the size during the process creation and allocates a contiguous chunk in the RAM for the process. This contiguous space is also called a segment. A virtual address is an offset in the segment. In this scheme, a virtual address can never be greater than the size of the process. MMU table now contains only one entry with two fields: base and limit. The base is the starting address of a process, and the limit is the size of the process. The VA to PA translation is done by merely adding the base to the VA.

## Slide 25: MMU
The OS decides the size of a process
  OS allocates a memory region of the given size for the process from RAM
  Each process has a base and limit
    base is the starting address of the region
    limit is the size of the process
  The virtual address space of the process is [0 - limit]
  PA = VA + base, where VA < limit

## Slide 26: Process1
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
 | base | limit | 
process1->base = alloc_from_ram(256);
process1->limit = 256;
Notes: MMU table's base and limit fields are set to the base and limit of the target process during scheduling. The OS maintains a metadata corresponding to each process. The process metadata contains the base and limit of the process. In this example, the OS sets the base and limit in process1's metadata with the starting address of process in RAM and 256.

## Slide 27: Process2
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
 | base | limit | 
process2->base = alloc_from_ram(512);
process2->limit = 512;
Notes: OS creates 512 bytes for process2 and sets the metadata accordingly.

## Slide 28: schedule
struct thread *ready_list;
struct thread *cur_thread;
void schedule() {
struct thread *prev = cur_thread;
struct thread *next = pop_front(ready_list);
cur_thread = next;
update_mmu_mappings(next);
context_switch(prev, next);
}

## Slide 29: update_mmu_mappings
// next process is process1
mmu->base = process1->base;
mmu->limit = process1->limit;
Notes: Before scheduling a new thread, OS sets the base and limit in the MMU table from the corresponding process’s metadata.

## Slide 30: update_mmu_mappings
// next process is process2
mmu->base = process2->base;
mmu->limit = process2->limit;

## Slide 31: MMU
The disadvantage of using this scheme is that the process can access only one segment (continuous region of memory)

## Slide 32: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
multiple regions
assert(VA < limit);
PA = VA + base
Notes: If we want multiple segments, then we need more entries in the MMU table. We also need a mechanism to tell the MMU, which entry to use for the translation.

## Slide 33: MMU
For multiple segments, we need to store the MMU table’s index to tell the hardware, which segment to look for the translation
  To store the index, x86 has six segment registers: %cs, %ds, %es, %ss, %fs, %gs
  All memory operands in x86 take a segment register
    default segment register for a memory operand is %ds
  The compiler generates the virtual addresses (an offset within a segment)
  MMU converts a virtual address to the physical address by adding the base of the segment to the virtual address
Notes: A segment register is used to store the index in the MMU table. Each memory access is associated with a segment register. The translation is done using the index in the segment register.

## Slide 34: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
Let us say, %eax contains 1000.
%ds contains index 1.
What is the physical address?
Notes: In this example, because the index in %ds segment register is 1, the second entry (with index 1) will be used for the translation. Because the limit of that particular entry is 128, and the virtual address in memory operand (%eax) is 1000 (which is greater than the limit), the hardware will generate some fault.

## Slide 35: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
Let us say, %eax contains 100.
%ds contains index 1.
What is the physical address?
3100
Notes: In this example, because the index in %ds segment register is 1, the second entry (with index 1) will be used for the translation. In this case, the virtual address is 100, which is less than the limit (128), the PA is computed by adding the base (3000) to the VA(100). So the physical address is 3100.

## Slide 36: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
multiple regions
assert(VA < limit);
PA = VA + base
MMU table is stored in the RAM.
Can we allow processes to modify the MMU table?
Notes: No, processes are not allowed to modify the MMU table; otherwise, they can access any physical address by changing the base and limit in the MMU table.

## Slide 37: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
multiple regions
assert(VA < limit);
PA = VA + base
MMU table is stored outside the base and limit of each entry in the table.

## Slide 38: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
multiple regions
assert(VA < limit);
PA = VA + base
MMU table is stored outside the base and limit of each entry in the table.
In this example, what are the physical addresses where the MMU table can’t be stored?
Notes: MMU table can’t be stored in physical addresses that belong to the ranges: [1000-1256], [3000-3128], and [8192-8192+4096].

## Slide 39: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
multiple regions
assert(VA < limit);
PA = VA + base
How does OS modify the MMU table then?
If the MMU is active, memory accesses are done using VA. There is no way to disable MMU.
Notes: OS memory accesses are also virtual because all memory accesses by CPU are done using virtual addresses. There is no way to disable MMU. To allow the modification of the MMU table by OS, we need to do something more.

## Slide 40: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | 
0 | 1000 | 256 | 
1 | 3000 | 128 | 
2 | 8192 | 4096 | 
3 | 0 | 0xffffffff | 
multiple regions
assert(VA < limit);
PA = VA + base
Adding a new entry to access everything will not help, because then the process can load its segment register with the new index.
Notes: One way of doing that would be to add a new entry to access any physical address, but that is not a valid solution because the user application can also access everything using that entry.

## Slide 41: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
multiple regions
assert(VA < limit);
PA = VA + base
The MMU table also contains DPL. A user process can only use indexes where DPL is 3.
Notes: The MMU table contains another field that contains the least privilege level required to access that entry, to prevent a user program from accessing the entry corresponding to OS (which allows access to entire physical address space).

## Slide 42: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
multiple regions
assert(VA < limit);
PA = VA + base
The MMU table also contains DPL. A user process can only use indexes where DPL is 3.
In this example, what are the indexes user application can load into its segment register?
Notes: User applications can not set its segment registers to use index 3, because only software running in ring-0 can use that index.

## Slide 43: MMU
MMU
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
VIRTUAL
ADDRESS
PHYSICAL
ADDRESS
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
multiple regions
assert(VA < limit);
PA = VA + base
In this example, after switching to ring-0, OS can set its segment register to use index 3.

## Slide 44: OS entry points
A user program can enter OS
  due to a system call
  due to interrupts and exceptions

## Slide 45: MMU
The MMU table discussed previously is called the global descriptor table (GDT)

## Slide 46: Global descriptor table (GDT)
The OS creates a GDT in memory
The GDTR register contains the base address of the GDT
lgdt instruction is used to load the GDTR
  lgdt instruction takes 6-byte memory operands
  4-byte base address (physical), and 2 bytes size
  lgdt is a privilege instruction
The GDT can have at most 213 entries

## Slide 47: GDT
Is it possible that the base address of the GDT is virtual?

## Slide 48: GDT
Is it possible that the base address of the GDT is virtual?
  No, GDT is used to translate a virtual address to physical address
  For translation, GDT need to know the base address of the GDT to fetch the base address at a given index
  If the base address of GDT is itself virtual then how hardware is supposed to convert it to the physical address
    it’s a chicken and egg problem

## Slide 49: Segment register
A segment register contains a 16-bit value
  The top 13 bits of segment registers contain the index in the GDT
  The lower 2 bits of the cs segment register contains the current privilege level (CPL)
    In user-mode, the last two bits of cs register is always 3
    In kernel-mode, the last two bits of cs register is always 0
  The hardware identifies the CPL using the lower 2 bits of the cs segment register
  User applications can’t directly modify the CPL
  CPL is changed during entry to the kernel

## Slide 50: Segment selector
GDT INDEX | 
0
2
15
Higher 13-bits in a segment register contains the index in the GDT table.

## Slide 51: Default segment register
cs is the default segment register for instruction pointer (EIP)
ss is default segment register of for stack pointer (ESP) and frame pointer (EBP)
ds is default segment register for memory operands (except those which contain esp and ebp)
es is default segment register in string instructions
fs and gs are optional can be explicitly used in memory operands

## Slide 52: Segmentation in practice
In practice, it is difficult to generate code using multiple memory regions having the same virtual addresses
Most compilers use only one region [base, limit]
  only one entry for process in the GDT
  all segment registers use the same index in GDT

## Slide 53: schedule
struct thread *ready_list;
struct thread *cur_thread;
void schedule() {
struct thread *prev = cur_thread;
struct thread *next = pop_front(ready_list);
cur_thread = next;
update_mmu_mappings(next);
context_switch(prev, next);
}

## Slide 54: update_mmu_mapping
How to implement update_mmu_mapping
  Only two entries in the GDT
  index 0 for the OS
  index 1 for the process
GDT[1].base = process.base;
GDT[1].limit = process.size;

## Slide 55: update_mmu_mapping
How to implement update_mmu_mapping, when processes want to use multiple entries in the GDT
  updating all entries in the GDT may be expensive
Create per-process GDT
  load the GDT corresponding to next process in update_mmu_mapping
    using lgdt

## Slide 56: update_mmu_mapping
execute_lgdt(process->gdt_base, process->gdt_limit);
Notes: If the number of GDT entries used by a process is too many, it is better to have a per-process GDT table instead of overwriting a single GDT table during scheduling. In this case, the GDT of the next process is loaded during schedule.

## Slide 57: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
mov $100, %ds:(%eax)
what is the PA, where
%eax = 100
%ds = (1 << 3) | 3;
Notes: The higher 13-bits in %ds contains 1. The PA is computed using adding base at index 1 (3000) to VA (100).

## Slide 58: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
10: mov $100, %ds:(%eax)
Let us say that the VA of mov instruction is 10.
what is the PA of mov, where
%cs = (2 << 3) | 3;
Notes: %cs is the default segment register for EIP. In this case, the EIP of mov instruction is 10. Because, the higher 13 bits in %cs register contains 2, PA corresponding to EIP can be obtained by adding 8192 to 10.

## Slide 59: Compiler
Does the compiler know the virtual addresses during compile time

## Slide 60: Compiler
Does the compiler know the virtual addresses during compile time
  Yes

## Slide 61: Compiler
Does the compiler know the virtual addresses during compile time
  Yes
Memory operands and instruction pointers are virtual addresses or physical addresses?

## Slide 62: Compiler
Does the compiler know the virtual addresses during compile time
  Yes
Memory operands and instruction pointers are virtual addresses or physical addresses?
  virtual addresses

## Slide 63: Compiler
Does the compiler know the virtual addresses during compile time
  Yes
Memory operands and instruction pointers are virtual addresses or physical addresses?
  virtual addresses
How they get converted to the physical address

## Slide 64: Compiler
Does the compiler know the virtual addresses during compile time
  Yes
Memory operands and instruction pointers are virtual addresses or physical addresses?
  virtual addresses
How they get converted to the physical address
  Each memory operand, EIP, ESP, etc., are associated with a segment register
  The top 13-bits in segment registers is an index in the GDT table
  The MMU hardware finds the base from the GDT entry corresponding to the index
  The base is added to the virtual address to get the physical address

## Slide 65: Global variable
int a;
foo() {
a = 0;
}
4: // a is allocated here
00000008 <foo>:
8: 55 push %ebp
9: 89 e5 mov %esp,%ebp
b: c7 05 04 00 00 00 00 movl $0x0,0x4
12: 00 00 00
15: 5d pop %ebp
16: c3 ret
Notes: Because the compiler statically knows the virtual address of global variables, it can generate code for directly accessing the global variables. Here the global variable is allocated at virtual address 4. The compiler can generate code to directly write to virtual address 4 that will be automatically get converted to the PA by the segmentation hardware at runtime.

## Slide 66: Global variable
int a;
foo() {
a = 0;
}
4: // a is allocated here
00000008 <foo>:
8: 55 push %ebp
9: 89 e5 mov %esp,%ebp
b: c7 05 04 00 00 00 00 movl $0x0,0x4
12: 00 00 00
15: 5d pop %ebp
16: c3 ret
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
At runtime, the OS sets all the segment registers to:
(2 << 3) | 3
before returning to user mode.
What is the address of a.
Which address movl $0x0, 0x4 will write to?
Notes: The mov will write to physical address 8196.

## Slide 67: call
foo() {
bar();
}
00000008 <foo>:
8: 55 push %ebp
9: 89 e5 mov %esp,%ebp
b: e8 02 00 00 00 call 12 <bar>
10: 5d pop %ebp
11: c3 ret
00000012 <bar>:
12: c3 ret
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
At runtime, the OS sets all the segment registers to:
(2 << 3) | 3
before returning to user mode.
What value will be pushed on the stack at call 12
Notes: The call instruction pushes the virtual address 0x10 on the stack.

## Slide 68: ret
foo() {
bar();
}
00000008 <foo>:
8: 55 push %ebp
9: 89 e5 mov %esp,%ebp
b: e8 02 00 00 00 call 12 <bar>
10: 5d pop %ebp
11: c3 ret
00000012 <bar>:
12: c3 ret
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
At runtime, the OS sets all the segment registers to:
(2 << 3) | 3
before returning to user mode.
Which address bar will return to when called from foo
Notes: The ret instruction jumps to the virtual address on the stack. The actual physical address translation of the return address is done using the %cs segment register. In this case, the physical address of the return address in foo is 8192 + 0x10.