## Slide 2: Optional assignment
sleep
wakeup
wait_for_all
thread_exit

## Slide 3: Next class
Homework 4 and 5 solutions
If we have time, I will take questions from the topics that have been covered until now

## Slide 4: Global descriptor table (GDT)
The OS creates a GDT in memory
The GDTR register contains the base address of the GDT
lgdt instruction is used to load the GDTR
  lgdt instruction takes 6-byte memory operands
  4-byte base address (physical), and 2 bytes size
  lgdt is a privilege instruction
The GDT can have at most 213 entries

## Slide 5: Segment register
A segment register contains a 16-bit value
  The top 13 bits of segment registers contain the index in the GDT
  The lower 2 bits of the cs segment register contains the current privilege level (CPL)
    In user-mode, the last two bits of cs register is always 3
    In kernel-mode, the last two bits of cs register is always 0
  The hardware identifies the CPL using the lower 2 bits of the cs segment register
  User applications can’t directly modify the CPL
  CPL is changed during entry to the kernel

## Slide 6: Segment selector
GDT INDEX | 
0
2
15
Higher 13-bits contains the index in the GDT table.

## Slide 7: Default segment register
cs is the default segment register for instruction pointer (EIP)
ss is default segment register of for stack pointer (ESP) and frame pointer (EBP)
ds is default segment register for memory operands (except those which contain esp and ebp)
es is default segment register in string instructions
fs and gs are optional can be explicitly used in memory operands

## Slide 8: schedule
struct thread *ready_list;
struct thread *cur_thread;
void schedule() {
struct thread *prev = cur_thread;
struct thread *next = pop_front(ready_list);
cur_thread = next;
update_mmu_mappings(next);
context_switch(prev, next);
}
Notes: The OS loads the GDT corresponding to the target process or updates the single GDT with the entries of the target process during scheduling.

## Slide 9: update_mmu_mapping
How to implement update_mmu_mapping, when processes want to use multiple entries in the GDT
  updating all entries in the GDT may be expensive
Create per-process GDT
  load the GDT corresponding to next process in update_mmu_mapping
    using lgdt

## Slide 10: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
what is the PA, where
%eax = 100
%ds = (1 << 3) | 3;
Notes: The higher 13-bits in %ds contains 1. The PA is computed using adding base at index 1 (3000) to VA (100).

## Slide 11: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
10: movl $100, %ds:(%eax)
Let us say that the VA of mov instruction is 10.
what is the PA of mov, where
%cs = (2 << 3) | 3;
Notes: %cs is the default segment register for EIP. In this case, EIP of mov instruction is 10. Because, the higher 13 bits in %cs register contains 2, PA of EIP can be obtained by adding 8192 to 10.

## Slide 12: Code isolation
How does OS prevent an application from directly jumping to its code

## Slide 13: Code isolation
How does OS prevent an application from directly jumping to its code
  OS code is stored outside the process address space

## Slide 14: Example
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
Which are the addresses where OS code is not present?
Notes: If the table shown on this slide is the current GDT, OS code can’t be present as physical addresses in the range [1000-1256], [3000-3128], and [8192-8192+4096].

## Slide 15: Interrupt_handler:
push %eax
push %edx
push %ecx
call schedule
pop %ecx
pop %edx
pop %eax
iret
CPU jumps to interrupt handler on interrupt. Can we use the same index in the cs register as the user program?
No, because OS code is outside the process address space (i.e., not mapped in the user-accessible GDT entries.)
Notes: On interrupt, the CPU needs to load the cs segment register with the value of the OS’s cs register before jumping to the target interrupt handler.

## Slide 16: Interrupt_handler:
push %eax
push %edx
push %ecx
call schedule
pop %ecx
pop %edx
pop %eax
iret
OS uses a different index in cs.
On interrupt, cs is set automatically to the OS’s index in GDT.
How does the hardware know the cs value of OS?

## Slide 17: Interrupt_handler:
push %eax
push %edx
push %ecx
call schedule
pop %ecx
pop %edx
pop %eax
iret
OS uses a different index in cs.
On interrupt, cs is set automatically to the OS’s index in GDT.
How does the hardware know the cs value of OS?
IDT contains cs:EIP pairs.

## Slide 18: Interrupt descriptor table (IDT)
IDT contains cs:EIP pairs
On interrupt 1, EIP is set to eip1 and cs is set to os_cs
os_cs:eip0
os_cs:eip1
os_cs:eipx
os_cs:eip255

## Slide 19: Interrupt
How does OS restore the cs of user program after returning from an interrupt?

## Slide 20: Interrupt
How does OS restore the cs of user program after returning from an interrupt?
  hardware pushes the cs on the stack before rewriting it with OS’s cs value
  iret restores the cs from the stack

## Slide 21: What about stack?
Can hardware push cs, eip, eflags on the user-program stack?

## Slide 22: What about stack?
Can hardware push cs, eip, eflags on the user-program stack?
  No, because of the following reason
  User program sets the %esp to a virtual address outside the limit of the %ss segment register and waits for an interrupt without accessing the stack
  After an interrupt, the CPU tries to push the cs, eip, eflags on an invalid address inside the ring-0 – causing the system to crash

## Slide 23: What about stack?
How does application thread wait for an interrupt without accessing the stack?
Notes: In this example, the application is setting the stack pointer to an invalid address and looping in an infinite loop. An interrupt at some point will force CPU to save the cs, eip, and eflags at an invalid stack location in ring-0, ultimately causing some bad things to happen.

## Slide 24: What about stack?
The OS can’t trust the user program stack pointer
The OS allocates a kernel stack for each user thread
The hardware automatically switches to the kernel stack on interrupt

## Slide 25: What about stack?
How does the CPU know, where is the kernel stack?

## Slide 26: What about stack?
How does the CPU know, where is the kernel stack?
  A special structure TSS contains the address of kernel’s stack and stack segment
    OS allocates the kernel stack and modifies the TSS before scheduling a new process

## Slide 27: schedule
struct thread *ready_list;
struct thread *cur_thread;
void schedule() {
struct thread *prev = cur_thread;
struct thread *next = pop_front(ready_list);
cur_thread = next;
update_tss(next->kstack, next->kss);
update_mmu_mappings(next);
context_switch(prev, next);
}
Notes: OS kernel creates a kernel stack corresponding to each user stack. During scheduling, the OS rewrites the kernel stack and stack segment values in the tss structure with the target process’ kernel stack pointer and stack segment.

## Slide 28: Kernel stack
Corresponding to every user stack, the OS allocates a kernel stack.
The starting address of the kernel stack is stored in the tss structure.
User stack : 4096 - 8192
Kernel stack : 8192 – 12228
tss->stack = 12228

## Slide 29: Kernel stack
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
USER STACK:
8000
Interrupt
KERNEL STACK
12228
push %eax
push %ecx
…
Is it okay if the hardware switches to a fixed stack pointer on every interrupt while switching from user to kernel?

## Slide 30: Kernel stack
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
USER STACK:
8000
Interrupt
KERNEL STACK
12228
push %eax
push %ecx
…
Is it okay if the hardware switches to a fixed stack pointer on every interrupt while switching from user to kernel?
Yes, on entry to the kernel, the stack is stateless. Similar to entry to main.

## Slide 31: Kernel stack
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
USER STACK:
8000
Interrupt
KERNEL STACK
12228
push %eax
push %ecx
push %edx
…
Is it okay if the hardware switches to a fixed stack pointer while switching from kernel to kernel due to an interrupt?
No, because it may overwrite the previous value on the kernel stack.
Interrupt
KERNEL STACK
12228
push %eax
push %ecx
…

## Slide 32: Kernel ss
Why we need a different stack segment for the kernel?
  Can we use the user’s stack segment in the kernel?
  Let us assume, for now, that the user application can’t change the ss segment

## Slide 33: Kernel ss
Why we need a different stack segment for the kernel?
  Can we use the user’s stack segment in the kernel?
  Let us assume, for now, that the user application can’t change the ss segment
If we execute, the kernel on user-stack the kernel local variables will be allocated on the user-stack that the user application can read after the interrupt handler returns
  This may potentially leak the other processes data
Notes: The question is, can we map the kernel stack in the process address space, i.e., the process can read/write to the kernel stack. However, the hardware will automatically set the stack pointer with the address of the kernel stack on interrupt.

## Slide 34: Kernel ss
void k_passwd_checker(char *passwd) {
char kbuf[128];
read_passwd(kbuf); // copy original passwd to kbuf
if (!memcmp(kbuf, passwd, 128)) // cmp passwd with user’s input
allow_access();
return error;
}
int u_main() {
request_access(“hello”);
}
Notes: In this example, u_main is the user routine, and k_passwd_checker is the kernel routine. k_passwd_checker reads the original password in its local variable kbuf (allocated on kernel stack) and compares the password with the user’s password. If they match, the OS provides access; otherwise, it returns an error status.

## Slide 35: Kernel ss
void k_passwd_checker(char *passwd) {
char kbuf[128];
read_passwd(kbuf); // read original passwd in kbuf
if (!memcmp(kbuf, passwd, 128)) // cmp passwd with user’s input
allow_access();
return error;
}
int u_main() {
request_access(“hello”);
// read stack to get the value of kbuf, call access again with correct passwd
}
u_main
Notes: Notice that the kbuf is allocated on the kernel stack, and after returning from the system call, the real password has been copied to kbuf, which is still there on the kernel stack. After returning from the system call, the user program can inspect the kernel stack (because it is in the process’ address space) to obtain the real password. It can again do the system call with the correct password to get access.

## Slide 36: Kernel ss
If the kernel uses the user’s ss, the user program can overwrite the return address on the stack to crash the system
  e.g., the user application can overwrite schedule1 with an invalid address to crash the system
  How?
foo
interrupt_handler
schedule1
schedule

## Slide 37: Kernel ss
If the kernel uses the user’s ss, the user program can overwrite the return address on the stack to crash the system
  e.g., the user application can overwrite schedule1 with an invalid address to crash the system
  How?
foo
interrupt_handler
schedule1
schedule
Even though the current thread is in the OS, the other threads of the current application can access the stack.

## Slide 38: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
foo was running
foo did write system call
interrupt was triggered
schedule1 was invoked
schedule was invoked
schedule picked bar
right now, context_switch is executing
foo
system_call
write
interrupt_handler
schedule1
schedule
Notes: Let us assume that the user application doesn’t corrupt the stack pointer, and the interrupt handler executes the OS on the user’s stack. Let’s say foo was the current thread, and it is being preempted due to a timer interrupt. The call stack at the start of the context_switch routine is shown on this slide.

## Slide 39: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
context_switch switches to bar’s stack
foo
system_call
write
interrupt_handler
schedule1
schedule
main
bar
interrupt_handler
schedule1
schedule

## Slide 40: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar returns to schedule
foo
system_call
write
interrupt_handler
schedule1
schedule
main
bar
interrupt_handler
schedule1

## Slide 41: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar returns to schedule1
foo
system_call
write
interrupt_handler
schedule1
schedule
main
bar
interrupt_handler

## Slide 42: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar returns to interrupt_handler
foo
system_call
write
interrupt_handler
schedule1
schedule
main
bar

## Slide 43: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar is running.
foo
system_call
write
interrupt_handler
schedule1
schedule
main

## Slide 44: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar is running
bar overwrites the stack of foo in a way that, return address of schedule is now 0xffffff00
foo
system_call
write
interrupt_handler
0xffffff00
schedule
main

## Slide 45: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
bar was executing
interrupt was triggered
scheduler picked foo
context_switch is called
right now, context_switch is executing
foo
system_call
write
interrupt_handler
0xffffff00
schedule
main
bar
interrupt_handler
schedule1
schedule

## Slide 46: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
context_switch switches to foo’s stack
foo
system_call
write
interrupt_handler
0xffffff00
schedule
main
bar
interrupt_handler
schedule1
schedule

## Slide 47: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
context_switch returns to schedule
foo
system_call
write
interrupt_handler
0xffffff00
main
bar
interrupt_handler
schedule1
schedule

## Slide 48: Kernel ss
unsigned *foo_stack;
int foo() {
int a;
foo_stack = &a;
write(1, “hello”, 5);
}
int bar() {
foo_stack[x] = 0xFFFFFFFF;
}
schedule1 returns to 0xffffff00
foo
system_call
write
interrupt_handler
0xffffff00
main
bar
interrupt_handler
schedule1
schedule
jmp to 0xffffff00
SYSTEM CRASH
Notes: Even though the current thread can’t change the return address inside the kernel, the other threads of the same process which are executing in the user-mode can change the return addresses of the other threads executing inside the kernel. For this reason, we must have to keep the kernel stack outside the process’ address space.

## Slide 49: Interrupt
How does OS restore the ss and esp of the user program after returning from an interrupt?

## Slide 50: Interrupt
How does OS restore the ss and esp of the user program after returning from an interrupt?
  ss and esp of user program is pushed automatically on the kernel stack by the hardware on switching from user to kernel
  iret restores the ss and esp from the stack when returning to the user mode

## Slide 51: ss and esp
Does the CPU need to switch stack when interrupted inside the kernel
interrupt_handler:
push %eax
push %ecx
push %edx
…
interrupt

## Slide 52: ss and esp
Does the CPU need to switch stack when interrupted inside the kernel
  why we did it for the user-program?
  why kernel can’t do the same thing?
interrupt_handler:
push %eax
push %ecx
push %edx
…
interrupt

## Slide 53: ss and esp
Does the CPU need to switch stack when interrupted inside the kernel
  why we did it for the user-program?
  why kernel can’t do the same thing?
interrupt_handler:
push %eax
push %ecx
push %edx
…
interrupt
If we switch the stack, the old value will be overwritten; no need to switch stack because kernel’s %esp and %ss are trusted.

## Slide 54: Interrupts in user-mode
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
Interrupt
k_ss:k_esp
CPU switches to kernel stack (k_esp) and ss (k_ss).
Notes: On switching from user to kernel, the hardware modifies %ss, %esp, %eflags, %cs, and %eip. The hardware pushes the old values of these registers on the kernel stack (after switching from user stack to kernel stack).

## Slide 55: Interrupts in user-mode
u_ss
u_esp
u_eflags
u_cs
u_eip
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
Interrupt
k_ss:k_esp
CPU switches to kernel stack (k_esp) and ss (k_ss).
CPU pushes user ss (u_ss)
CPU pushes user esp (u_esp)
CPU pushes user flags (u_eflags)
CPU pushes user cs (u_cs)
CPU pushes user eip (u_eip)

## Slide 56: Interrupts in kernel-mode
%eax
%ecx
o_eflags
o_cs
o_eip
interrupt_handler:
push %eax
push %ecx
push %edx
call schedule1
pop %edx
pop %ecx
pop %eax
ret
Interrupt
esp before interrupt
CPU doesn’t switch stack.
CPU pushes old flags (o_eflags)
CPU pushes old cs (o_cs)
CPU pushes old eip (o_eip)
Notes: On interrupt in the kernel, the hardware doesn’t switch stacks. So, the hardware pushes only three values: %eflags, %cs, and %eip on the kernel stack before overwriting them.

## Slide 57: Current privilege level
How does CPU know the current privilege level (CPL)?
  The last two bits of the cs register contain the CPL

## Slide 58: iret to kernel-mode
%eax
%ecx
o_eflags
o_cs
o_eip
interrupt_handler:
push %eax
push %ecx
push %edx
call schedule1
pop %edx
pop %ecx
pop %eax
ret
Interrupt
esp before
iret
CPU restores eip, cs, and eflags from the stack
pop %eip
pop %cs
pop %eflags
Notes: On iret to kernel-mode, the hardware pops three values.

## Slide 59: iret to user-mode
u_ss
u_esp
u_eflags
u_cs
u_eip
foo:
push %ebp
mov %esp, %ebp
mov $1, %eax
mov %ebp, %esp
pop %ebp
ret
Interrupt
CPU restores five values from the stack:
pop %eip
pop %cs
pop %eflags
pop %esp
pop %ss
esp before
iret
Notes: On iret to user-mode, the hardware pops five values.

## Slide 60: iret
How does CPU know how many values to pop (five or three)?

## Slide 61: iret
How does CPU know how many values to pop (five or three)?
  After popping cs register if the last two bits in cs register is 3, it means that iret is returning to the user mode
    In this case, CPU pops five values; otherwise, CPU pops three values

## Slide 62: First process
How does the first process return to the user-mode?

## Slide 63: First process
u_ss
u_esp
u_elags
u_cs
u_main
CPU restores five values from the stack:
pop %eip
pop %cs
pop %eflags
pop %esp
pop %ss
After, iret the CPU jumps to main of the first process.
esp before
iret
OS manually setup the kernel stack before iret
Notes: For the first process, the OS allocates a kernel stack, manually puts five values corresponding to the new thread on the kernel stack, sets the %esp to the newly created kernel stack, and executes the iret instruction.

## Slide 64: Segmentation
What happens if a user-application accesses a virtual address that is outside the limit of the segment?
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
what is the PA, where
%eax = 1000
%ds = (1 << 3) | 3;

## Slide 65: Segmentation
What happens if a user-application accesses a virtual address that is outside the limit of the segment?
  What is the problem with crashing the system?
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
what is the PA, where
%eax = 1000
%ds = (1 << 3) | 3;
Notes: If we bring down the whole system when an application accesses an invalid address, then any process can bring the whole system down.

## Slide 66: Segmentation
What happens if a user-application accesses a virtual address that is outside the limit of the segment
  The hardware generates an exception called general protection fault
idx | base | limit | DPL
0 | 1000 | 256 | 3
1 | 3000 | 128 | 3
2 | 8192 | 4096 | 3
3 | 0 | 0xffffffff | 0
movl $100, %ds:(%eax)
what is the PA, where
%eax = 1000
%ds = (1 << 3) | 3;
Notes: We will discuss exceptions in the next class.